Final Report to the State Water Resources Control Board

Agreement number 01-269-250-0

Libby Raskin, Michael J. Singer, and Angela DePaoli

June 18, 2004

REVISED SEPTEMBER 20, 2004

The mention of manufacturers, trade names or product names does not imply recommendation or lack of recommendation of use of these products or manufacturers by the University of California, the authors of this report or State of California.

Final Report to the State Water Resources Control Board

Agreement number 01-269-250-0

Executive Summary

To investigate the types and amounts of materials used for erosion and dust control on California construction sites, we examined product data, surveyed contractors and manufacturers, reviewed Storm Water Pollution Prevention Plans and inspected construction sites.

Findings

- Over 394 erosion control and dust suppressant products are available to contractors.

- Our survey showed that wattles are the most widely used erosion control product followed by blankets, mulch, and liquid or powder products.

- Building materials and construction waste exposed to storm water can leach harmful constituents.

- Selection of cost effective water sampling & monitoring methods for construction sites are site specific.

- More than half of construction sites visited show poor housekeeping, best management practice non-compliance and lack of BMP maintenance.

- Almost half of the examined SWPPPs were inadequate.

- The California Water Resources Control Board SWPPP database is not up-to-date or maintained.

- Oversight of the SWPPP process is lacking.

- The most effective deterrents to sediment and pollutant release from construction sites combine education and enforcement.

## Recommendations

- Encourage good construction site housekeeping including installation and maintenance of BMPs.

- Encourage contractors to choose dust suppressant and erosion control materials with low water solubility and low concentrations of harmful constituents that will biodegrade and not bioaccumulate.

- Decrease exposure of building materials and construction waste to storm water by requiring covered waste receptacles and stockpiles. Make use of Spanish labeling on these receptacles.

- Maintain soil infiltration rates by reducing compaction during construction activity.

- Renovate badly compacted soil to increase infiltration rates.

- Maintain soil cover to reduce soil erosion whenever possible.

- Educate day-laborers, in Spanish if necessary, on proper BMP installation and maintenance.

- Implement electronic submittal of SWPPPs.

- Improve SWPPP preparation and phasing of BMP installation.

- Require that SWPPPs be site specific and increase inspections.

- Implement a “maid service” to provide maintenance of erosion control and good housekeeping practices

- Maintain drain inlets to reduce sediment entry into drains.

- Maintain regular street sweeping operations to reduce sediment entry into drains.

- Maintain wattles and other erosion control materials during construction activities.  In particular, do not drive over or remove wattles during construction.

- Require submission of storm water runoff test results to California WRCB and develop database for construction site storm water runoff pollution.

- Develop and implement a testing program for all materials used for erosion control or dust suppression to determine potential toxicity.

Table of contents

Subject	Page

Executive summary		2

Table of contents		4

Introduction		7

Task 1 Compilation of information		8

Table 1 List of Access 2000 tables			9

Table 1a Product list summary		14

Task 2 Investigate rates of application		15

Table 2 Number of survey respondents		15

Table 3 Percentage of respondents using specific materials		16

Table 3a Manufacturer summary of products sold in California		16

Table 4 Respondents by county or region		18

Table 5 Product use summary for 2002 by product category		20

Table 6 Number of users and quantities of blankets used in 2002		21

Table 7 Number of users and quantities of dust suppressants in 2002		22

Table 8 Number of users and quantities of lime & fly ash in 2002		22

Table 9 Number of users and quantities of mulch and fiber in 2002		23

Table 10 Number of users and quantities of soil binders and tackifiers

used in 2002		24

Table 11 Number of users and quantities of wattles used in 2002		25

Table 12 Number of users and quantities of miscellaneous materials

used in 2002		25

Table 13 Number or respondents reporting product brand names	26

Table 14 Brand name use 	26

Table 15 Brand composition: Liquids and powders	29

Table 16 Brand composition: Mulch and fibers	30

Table 17 Brand composition: Blankets	31

Table 18 Contractor and manufacturer application rate comparison	32

Table 19 Comments made by survey respondents	33

Task 3 Perform background search on storm water impacts from construction

Materials	39

Table 20 Building material pollutants	40

Table 21 Green dye water solubility and aquatic toxicology	42

Task 4 Determine what current good housekeeping best management

practices are used	43

Table 22 SWPPP scoring system	44

Table 23 Classification of responses to request for SWPPPs	45

Table 24 Number of SWPPPs by type, designer and quality	45

Table 24a SWPPP Quality by Designer	46

Table 25 Number of each kind of BMP recommended and used	46

Table 26 Number of sites visited and the stage of construction of

each active site	47

Table 27 Number of each type of non-compliance found at

construction sites	48

Subject		Page

Task 5 Develop and or propose new alternative strategies	49

Task 6 Draft cost-effective and fair methodology for storm water sample

collection and analysis report	57

Table 28 Sampling device, monitoring equipment and laboratory fee

data fields in the Access tables	59

Table 29 Example of storm water sampling device characteristics	62

Table 30 Example of water monitoring equipment table	63

Table 31 Average price and price range of laboratory tests	65

Table 32 Survey product information from manufacturer	68

Table 33 Survey product chemical, solubility and toxicity information	70

Task 7 Final version of the report	72

Final summary	72

Erosion and dust control materials on construction sites	72

Building materials on construction sites	73

Best management practices on construction sites and SWPPPs	74

BMP non-compliance on construction sites	74

SWPPP issues	74

Strategies to reduce impacts from erosion control materials and construction

materials on storm water	74

Mulch and fibers	75

Dust suppressants	76

Tackifiers and soil binders	75

Materials with green dye	76

Other education and enforcement strategies	76

References	76

Appendices	83

Appendix 1	Erosion control professional survey	84

Appendix 2	SWPPP draft inspection report	85

Appendix 3	Letter requesting SWPPP from contractors	94

Appendix 4	Tables from the Access database	95

Table 34 Application Rate		96

Table 35 Ash Aquatic Toxicity		105

Table 36 Bibliography	106

Table 37 Blankets Product Data	113

Table 38 BMP Manuals	116

Table 39 BMP Table	118

Table 40 Brand Name Usage	124

Table 41 Chemical List	127

Table 42 Contractor Survey General Category Use	137

Table 43 Element Aquatic Toxicity	141

Table 44 Erosion Control Specialist General Category Use	143

Table 45 Green Dye Toxicology	144

Table 46 IECA General Category Use	145

Table 47A Laboratory Fees Part 1	146

Table 47B Laboratory Fees Part 2	147

Table 47C Laboratory Fees Part 3	148

Table 47D Laboratory Fees Part 4	149

Table 47E Laboratory Fees Part 5	150

Table 47F Laboratory Fees Part 6	151

Table 47G Laboratory Fees Part 7	152

Table 48 Laboratory Fee Summary	153

Table 49 Liquids & Powders Chemical Data	154

Table 50 Liquids & Powders Product Data	161

Table 51 Manufacturer Survey General Data	176

Table 52A Manufacturers Part 1	177

Table 52B Manufacturers Part 2	182

Table 53 Manufacturers Survey Products Sold	192

Table 54 Mulch Chemical Data	194

Table 55 Mulch Product Data	196

Table 56 Pollutants (Building Materials)	198

Table 57 Product List	203

Table 58 Product Testing Sources	221

Table 59 Respondent Use By Region	226

Table 60A Survey Data Part 1	228

Table 60B Survey Data Part 2	246

Table 61 SWPPP and Construction Site BMPs	269

Table 62A SWPPP and Construction Site Data Part 1	270

Table 62B SWPPP and Construction Site Data Part 2	275

Table 63A Water Monitoring Equipment Part 1	279

Table 63B Water Monitoring Equipment Part 2	283

Table 63C Water Monitoring Equipment Part 3	285

Table 63D Water Monitoring Equipment Part 4	290

Table 64A Water Sampling Devices	292

Table 64B Water Sampling Devices	293

Introduction

This is the final report on agreement number 01-269-250-0.  The project consists of seven tasks directed at determining the types and amounts of materials being used for dust suppression and erosion control on California construction sites.  The majority of the work has been done by Libby Raskin, a post-graduate researcher and Angela DePaoli, a graduate student researcher working with Professor Michael J. Singer in the Department of Land, Air and Water Resources.  An electronic version of this report and all of the Microsoft Access tables will be available on line at http://erosion.lawr.ucdavis.edu.  In this report we describe the processes used to obtain information and provide the findings for each of the tasks.

Erosion control management has proven to be a difficult task for many construction sites, both in California and outside, as reflected in numerous reports of inadequate SWPPPs and BMP non-compliance. In addition, ineffective BMPs, either by design, improper installation or lack of maintenance, exacerbate the challenge of controlling erosion and sediment from construction sites.

The following examples of problems observed at construction sites in California provide background for our study and final recommendations. References cited in this report can be found starting on page 73.

In 1997, the San Francisco Bay Regional Water Quality Control Board aggressively investigated construction site erosion control practices (Mumley, 2000). Common observations included no permit on site, deficient or undeveloped SWPPPs, non-implemented SWPPPs, and improper and ineffective erosion control measures. As a result of these findings, the Regional Board reported that increased enforcement and education has improved NPDES permit compliance to greater than 90%.

In contrast to the subsequent improvements reported by the SF Regional Board, is the November 2000 investigation by the Santa Clara Valley Audubon Society (SCVAS) of dozens of active construction sites larger than 5 acres in Santa Clara County, also within the SF Bay Water Quality Control Region (SCVAS, 2002). Using video and still cameras, the investigators found that an overwhelming majority of the sites were in violation of the Clean Water Act during the 2000-01 and 2001-02 rainy seasons. Although City of San Jose inspectors routinely observed violations, the report states that stiff enforcement action or regular monitoring of problems was rare. In addition to failing and inappropriate BMPs, the investigator’s review of construction site SWPPPs showed much variation in adequacy. Furthermore, document retrieval from the City of San Jose proved frustrating throughout the duration of the investigation due to inconsistent and disorganized record keeping.

In other locations, similar problems have been found.  For example, a 1994 investigation of 128 North Carolina construction sites found that 16% of BMPs in erosion control plans were not implemented. BMP failure resulted from technical inadequacy, poor installation, or poor maintenance. Of those that were implemented and that failed, 55% were not installed properly, 27% were poorly maintained, and 18% were technically inadequate. The report comments that installation problems often occur when erosion control plans contain vague field information and the construction crews lack proper training (Paterson, 1994).

An April 1998 inspection sweep of 363 construction sites by the North Carolina Division of Land Resources (NCDLR) found 22% not in compliance and 19% causing offsite sedimentation (NCDLR, 1998).

In a 1993 survey of 62 state highway erosion control experts, 30% reported that at least 50% of BMPs specified in highway erosion control plans were never installed and 20% indicated that 50-75% were installed. Only 21% stated that 100% of erosion control plan BMPs were installed (Mitchell, 1993).

Inadequate clearing and grading ordinances in many communities may contribute to poor construction site erosion control. In a survey of 43 local government programs, 44% of respondents indicated that soils were often still exposed after their time-limit expired, 56% reported that revegetation efforts were frequently unsuccessful due to poor planting or seeding techniques, 44% indicated that cleared slopes were not adequately stabilized, 33% noted that no time-limit was imposed for revegetation, and 67% stated that erosion and sediment controls were not adequately maintained (Corish, 1994).

A survey of 810 construction sites by the Maine Department of Environmental Protection (MDEP) found 46% of residential sites, 38% of commercial sites and 33% of road construction sites not in compliance with Maine’s Erosion and Sediment Control Law. The survey showed that the smaller the site and the flatter the site, the more likely for it to be in compliance. In addition, sites close to a natural resource were less likely to be in compliance (56%) compared to those far from a natural resource (53%), even though the closer sites were more likely to use BMPs (MDEP, 2004).

A survey sponsored by the Montana Department of Transportation of personnel from 16 state DOTs found that improper BMP installation was the main cause of erosion and sediment discharge. In addition, the most prevalent reason for the difficulties and breakdowns in BMP installation was lack of training and communication in field personnel (MDOT, 2003).

Other countries also battle with erosion control non-compliance. The Brisbane City Council (Australia) monitored construction sites for four years and found that only 50% met erosion and sediment control requirements (Taylor, 2002).

Task 1.  Compilation of information

This task directed us to compile a comprehensive list of soil amendments, soil treatments and other materials used or applied in large quantities, applied frequently, and/or meant to be applied during the rainy season in the State of California to construction sites.

We did a comprehensive search of the literature, and of web sites to find the kinds of materials that could be used for erosion and dust control on construction sites.  We created a Microsoft Access 2000 database containing 31 tables to catalog the information (Table 1 and the web site).  We found 458 products and list 185 manufacturer’s names and contact information for the manufacturers.  The products have been sorted into categories of similar materials including blankets, liquids and powders, and mulch products (Table 1a).  Few have created other tables that provide information on recommended application rates and toxicity of materials.

Table 1.  List of Access 2000 tables on the web site and in the appendix.

| Table Number | Table Name | Subject | Record Count | Fields |
| --- | --- | --- | --- | --- |
| 34 | Application Rate | Manufacturer recommended application rate for liquids, powders and mulch erosion control products | 276 | Brand Name, Application Rate, Product ID |
| 35 | Ash Aquatic Toxicity | LC50 and EC50 values for several fly ash and MSWI ash samples | 13 | Material Type, Material Source, Toxicity, Data Source |
| 36 | Bibliography | References cited in report | 109 | ID, Author 1, Reference |
| 37 | Blankets Product Data | General composition of brand name erosion control blankets | 102 | Brand Name, General Composition, Product ID |
| 38 | BMP Manuals | BMP manuals examined in report | 14 | Code, Agency, State, Year, Title, Pages, www |
| 39 | BMP Table | BMPs described in BMP manuals | 171 | BMP Name, 13 fields for 13 BMP Manuals |
| 40 | Brand Name Usage | Brand name products used by respondents in survey | 36 | Brand Name, Product ID, General Composition, Number of Users, Number of Users Reporting Amount, Total 2002 Amount |

Table 1. (continued)

| Table Number | Table Name | Subject | Record Count | Fields |
| --- | --- | --- | --- | --- |
| 41 | Chemical List | Chemicals listed in MSDS of products in Product List table | 81 | Chemical Name, CAS No., Formula, Water Solubility, Toxicity |
| 42 | Contractor Survey General Category Use | General categories of products used by respondents in Contractor Survey | 134 | Contractor ID, Tackifiers, Soil Binders, Soil Drying Agents, Mulch, Blankets etc., Wattles etc., Dust Suppressants |
| 43 | Element Aquatic Toxicity | One to four LC50 or EC50 values for 18 metals | 18 | Element Name, CAS Number, Toxicity 1, Toxicity 2, Toxicity 3, Toxicity 4 |
| 44 | Erosion Control Specialist General Category Use | General categories of products used by respondents in Erosion Control Specialist Survey | 31 | ECS ID, Tackifiers, Soil Binders, Mulch, Blankets etc., Wattles etc., Dust Suppressants |
| 45 | Green Dye Toxicology | Solubility and LC50 values for green dyes used in mulch and tackifier | 7 | ID, Dye Name, CAS No., Water Solubility, Aquatic Toxicology, Data Source |
| 46 | IECA General Category Use | General categories of products used by respondents in IECA Survey | 26 | IECA ID, Tackifiers, Soil Binders, Soil Drying Agents, Mulch, Blankets etc., Wattles etc., Dust Suppressants |
| 47 | Laboratory Fee Summary | Price range and avg. price of tests in Laboratory Fee table | 26 | Lab Test Name, Average Price, Price Range |

Table 1. (continued)

| Table Number | Table Name | Subject | Record Count | Fields |
| --- | --- | --- | --- | --- |
| 48 | Laboratory Fees | Prices for various storm water pollutant tests from six laboratories | 6 | ID, County, Turnaround, TSS, Settable Solids, Turbidity, Oil & Grease, pH, Conductivity, TDS, Alkalinity, Residual Chlorine, VOCs, SVOCs, Phenols, MBAS, Phosphates, Phosphorus, Pesticides, Herbicides, Metals (Title 22), Chromium VI, Metals (Individual), NO3, NH3, BOD, COD, TOC, Total Coliform |
| 49 | Liquids & Powders Chemical Data | Connector between Liquids & Powders Product Data table and MSDS Chemical List table | 292 | Brand Name, Product ID, Chemical ID |
| 50 | Liquids & Powders Product Data | Manufacturer supplied composition, solubility, pH and ecological information for liquid and powder products | 212 | Brand Name, General Composition, Ecological Info, pH, Water Solubility, Product ID |
| 51 | Manufacturer Survey General Data | General categories of products sold in California | 32 | Manufacturer ID, Tackifiers, Soil Binders, Mulch, Blankets etc., Wattles etc., Dust Suppressants |

Table 1. (continued)

| Table Number | Table Name | Subject | Record Count | Fields |
| --- | --- | --- | --- | --- |
| 52 | Manufacturers | Manufacturers of products in Product List table and in survey | 185 | Company Name, Contact Name, Telephone, Address, www, Company ID |
| 53 | Manufacturers Survey Products Sold | Amounts sold in CA of general erosion control materials, 2002 | 62 | Product Type, Material, Amount Sold, Year |
| 54 | Mulch Chemical Data | Connector between Mulch Product Data table and MSDS Chemical List table | 76 | Brand Name, Product ID, Chemical ID |
| 55 | Mulch Product Data | Manufacturer supplied composition information | 64 | Brand Name, General Composition, Product ID |
| 56 | Pollutants (Building Materials) | Constituents found in building material leachates | 117 | ID, Material, Category, Use, Constituents, Water Source, Data Source |
| 57 | Product List | Brand name list of erosion control products, dust suppressants and waste materials | 458 | Brand Name, Use, Type, MSDS, Product ID, Company ID |
| 58 | Product Testing Sources | Organizations that test erosion control products; includes summaries of relevant research studies | 7 | Organization, Report Name, Report Summary, Report Details, www |
| 59 | Respondent Use By Region | Counties and regions of California in which survey respondents used products | 50 | County/Region, Respondent Count |

Table 1. (continued)

| Table Number | Table Name | Subject | Record Count | Fields |
| --- | --- | --- | --- | --- |
| 60 | Survey Data | Compilation of specific data in all surveys | 493 | ID, Product Type, Brand Name, Product ID, Total 2002 Amount, Contractor Application Rate, Manufacturer Application Rate, County/Region, City, Location Type, Comments |
| 61 | SWPPP and Construction Site BMPs | Best management practices indicated in SWPPPs and found on construction sites | 27 | ID, BMP Type, Number of SWPPPs Using BMP, % of SWPPPs, Number of Sites Using BMP, % of Sites |
| 62 | SWPPP and Construction Site Data | Specific information about SWPPPs and observational information about construction sites | 32 | ID, Acreage, Map Indicates BMP Type and Location, Type of Site, SWPPP Designer, SWPPP Comments, Quality of SWPPP, Site Visit Comments, BMPs Used On-Site, Non-Compliance BMP Type |

Table 1. (continued)

| Table Number | Table Name | Subject | Record Count | Fields |
| --- | --- | --- | --- | --- |
| 63 | Water Monitoring Equipment | Portable water- monitoring- equipment product data | 46 | Product Name, Product Type, Analytes, DO, pH, Conductivity, ORP, Turbidity, Resistivity, Salinity, TDS, Total Dissolved Gas, Depth, Barometric Pressure, Temperature, GPS, Price, Power Source, Memory, Range, Communication, Unattended Logging, www |
| 64 | Water Sampling Devices | Automatic and mechanical water sampling device product data | 12 | Product Name, Product Type, Price, Weight, Power Source, Telemetry, www, Notes |

Table 1a: Product List Summary

| Product Type | Product Count |
| --- | --- |
| Bags | 2 |
| Blankets | 102 |
| Cement Kiln Dust Materials | 5 |
| Coal Combustion Products | 59 |
| Geofibers | 1 |
| Liquids & Powders | 213 |
| Mulch | 64 |
| Rolls, Logs & Wattles | 12 |
| Total | 458 |

Task 2.  Investigate and report the recommended and actual rates of application, the potential for entering runoff, and any non-label use of construction materials.

We created three one-page survey instruments that were sent to 1378 contractors, 204 erosion control specialists (names were obtained from the CPESC, Inc., for Erosion Control Specialists certified in California), and 199 California members of the International Erosion Control Association, to determine what materials were being used in California and their actual rates of use. A fourth survey was sent to 151 manufacturers to identify the kinds and amounts of erosion control materials sold in California. An example of one survey is in Appendix 1 at the end of this report. Our Contractor list came from the SWPPP applicant database on the State Water Resources Control Board website. From this database, we selected for company names with the word “contractor” or “homes” and that applied for a permit in 2002. The 151 manufacturers surveyed came from our own list.  Table 2 summarizes the responses received from the three user survey groups.  Seventy of the 261 responses contained no information and 36 respondents (191-155) provided only general information from the top of the survey.  We used the remaining detailed data in the analysis that follows. We feel that the response rate was very good, as surveys often don’t generate a return rate of more than 10%.  Respondents to this survey include erosion control professionals, consultants, engineers, agency officials, contractors, and a farmer. Table 2 summarizes the response data for all three surveys. The subsequent tables report on the detailed results from the surveys that contained useable data.

Table 2. Number of respondents, and percentage responding from all surveys.

| Survey Type | Number Sent | Number Returned | Surveys with No Data | Surveys with General Data | Surveys with Specific Data | Surveys with County or Region Data |
| --- | --- | --- | --- | --- | --- | --- |
| Contractor | 1378 | 185 (13%) | 51 | 134 | 114 | 91 |
| ECS | 204 | 43 (21%) | 12 | 31 | 23 | 20 |
| IECA | 199 | 33 (17%) | 7 | 26 | 18 | 16 |
| Total |  | 261 | 70 | 191 | 155 | 127 |

Table 3 is a summary of the product use and products sold data from respondents in all four surveys.  The amounts and types of products sold in California from the 32 Manufacturer respondents are listed in Table 3a. In addition to the data in Table 3, the three user surveys also provided more detailed information about where materials are used, rates of application, brand names and amounts used in 2002. The more specific data are contained in the Access table called Survey Data (155 respondents for 493 products) and are most easily described by reviewing and summarizing the data in each field: County/Region, Product Type, Brand Name, Total Amount Used 2002, Contractor Application Rate, Manufacturer Application Rate, Location Type, Comments.  All surveys containing specific data for any of the fields are included in this table. In the following paragraphs and tables, we summarize the data by these categories.

Among the respondents, rolls, logs and wattles were the most frequently used materials for erosion control. These materials were followed by blankets, mulches and tackifiers.  Soil binders, drying agents and dust suppressants were much less frequently reported as being used.

Table 3. Percentage of Contractors, ECS and IECA respondents who use specific classes of materials and percent of manufacturers selling materials in California.

| Material | Contractors | ECS | IECA | Manufacturers |
| --- | --- | --- | --- | --- |
|  | (% using the material) |
| Tackifiers | 21 | 37 | 69 | 53 |
| Soil binders | 13 | 13 | 19 | 44 |
| Soil drying agents | 19 | NA | 8 | No data |
| Mulch | 45 | 87 | 77 | 16 |
| Blankets | 57 | 73 | 81 | 19 |
| Rolls, logs, wattles | 82 | 80 | 92 | 19 |
| Dust suppressants | 38 | 27 | 31 | 53 |

NA not applicable

Table 3a. Manufacturer survey summary of products sold in California.

| Material | 2001 | 2002 | Other |
| --- | --- | --- | --- |
| Bags (geotextile) |  | 5,000 units |  |
| Blankets, etc. |  | 2,778,650 sq. yds. + 1,172,241 lbs. |  |
| Liquids & Powders (asphalt emulsion) |  | 5,000 gallons |  |
| Liquids & Powders (calcium lignosulfonate) | 30 x 55 gallon drums |  |  |

Table 3a. (continued)

| Material | 2001 | 2002 | Other |
| --- | --- | --- | --- |
| Liquids & Powders (enzyme stabilizer) | 160 gallons | 160 gallons |  |
| Liquids & Powders (magnesium chloride) | 250 gallons + 1158 tons | 500 gallons + 580 tons |  |
| Liquids & Powders (polymers, acrylic or polyacrylamide) | 8,097 lbs. + 440 gallons | 301,641 lbs. + 140,000 gallons | 3,400 gallons (1997-2003) |
| Liquids & Powders (resin emulsion) |  | 21,067 gallons |  |
| Liquids & Powders (tall oil) | 300 tons | 400 tons |  |
| Liquids & Powders (vegetable product) |  | 3,315 lbs. | 840 lbs. (2003) |
| Liquids & Powders (tackifiers/stabilizers, material unknown) | 1,224 lbs. | 4,000 lbs. + 22,176 gallons |  |
| Mulch (wood and recycled fiber) | 10,254.5 tons | 10,112 tons + 1,250 cubic yards |  |
| Rolls, Logs, Wattles | 1,447,317 linear feet | 7,829,312 linear feet + 204,000 lbs. |  |

County/Region summary

Most respondents with specific information (127, 82%) report a location of use for their products, usually a county and/or city, although some report a region. The locations span 44 counties and 6 regions. The Access table called Respondent Use by Region organizes these data in addition to their original location in the Survey Data table. See Table 4 for county and region data. Some respondents use products in several regions.

Table 4. Respondents by county or region sorted by number of respondents in each area.

| County/Region | Respondent Count | County/Region | Respondent Count |
| --- | --- | --- | --- |
| San Diego | 18 | Amador | 2 |
| Riverside | 13 | Monterey | 2 |
| Orange | 12 | Mendocino | 2 |
| Placer | 10 | Yuba | 2 |
| Contra Costa | 9 | Trinity | 2 |
| Sacramento | 9 | San Luis Obispo | 2 |
| Napa | 8 | Humboldt | 1 |
| Los Angeles | 7 | Tehama | 1 |
| Alameda | 7 | Santa Barbara | 1 |
| Santa Clara | 6 | Sutter | 1 |
| Ventura | 6 | Siskiyou | 1 |
| Sonoma | 6 | Calaveras | 1 |
| Statewide | 5 | Northern California | 1 |
| Stanislaus | 5 | San Francisco | 1 |
| Solano | 5 | Merced | 1 |
| San Joaquin | 5 | Tuolumne | 1 |
| Santa Cruz | 5 | Fresno | 1 |
| El Dorado | 4 | Modoc | 1 |
| Marin | 4 | Lassen | 1 |
| Shasta | 4 | Tulare | 1 |
| Southern California | 4 | Madera | 1 |
| San Mateo | 4 | Central California | 1 |
| Butte | 3 |  |  |
| San Bernardino | 3 |  |  |
| Yolo | 2 |  |  |
| Central Coast | 2 |  |  |
| Bay Area | 2 |  |  |
| Lake | 2 |  |  |

Products Use and Amounts by Type Summary

Product types are listed in the Survey Data table as specifically as provided by the respondent. Not all respondents report an amount. When they do, the units are not consistent and may be posted as “lots”, acres, gallons, linear feet, square feet, cubic yards, number count, or tons. Of the materials listed in the Survey Data table, 389 (79%) include an amount. The following tables show the number of users for each product type, the number of users posting an amount for the product type, and the amount used for each type. Since contractors may use more than one type within a category, the number of users for the general category that report an amount is also indicated.  Tables 6 through 12 organize the product types, user number, and amount data by category for Blankets, Dust Suppressants, Lime & Fly Ash, Mulch & Fibers, Binders & Tackifiers, Wattles, and Miscellaneous. Table 5 summarizes the amount data by user number and general category.

Table 5. Product use summary for 2002 sorted by product category.

| Category | Total Amount 2002 | Number of Respondents for Total Amount |
| --- | --- | --- |
| Blankets | 266 acres; 6,052 rolls; 5,100 lbs.; 16,710 linear feet | 70 |
| Binders & Tackifiers | 2,297 acres; 258 tons; 25 road miles; 117,720 gallons | 35 |
| Fly Ash | 1 ton; 20 cubic yards | 3 |
| Lime | 3,540 tons; 31 acres; 500-1,000 sacks; 120 cubic yards | 15 |
| Mulch & Fibers | 1,873 acres; 2,133 tons; 200 gallons; 1,317 bales; 31,810 cubic yards | 59 |
| Wattles | 11 tons; 27 pallets; 21,005 rolls; 1,444,035 linear feet | 103 |

Tables 6 through 12 are more detailed summaries of the amounts of materials used sorted by type of material.

Table 6. Number of users and quantities of different blanket materials used in California in 2002.

| Product Type: Blankets | Number of Users | Number of Users Reporting Amount | Amount |
| --- | --- | --- | --- |
|  | C | IECA | ECS | Total |  | Acres | Rolls | Lbs. | Linear Feet | Square Feet |
| Blankets (unspecified) | 13 | 4 | 7 | 24 | 20 | 28 | 47 | 1,500 | 3,000 | 2,429,400 |
| Blankets, coconut fiber | 4 | 1 | 5 | 10 | 9 |  | 522 |  |  | 906,080 |
| Blankets, excelsior or straw |  | 1 |  | 1 | 0 |  |  |  |  |  |
| Blankets, fabric | 1 |  |  | 1 | 1 |  | 9 |  |  |  |
| Blankets, geotextile | 7 |  |  | 7 | 4 |  |  |  | 150 | 390,900 |
| Blankets, hemp |  |  | 1 | 1 | 1 |  | 2 |  |  |  |
| Blankets, jute | 5 |  |  | 5 | 5 |  |  |  | 10,560 | 1,875,000 |
| Blankets, mat | 1 |  |  | 1 | 1 |  |  |  |  | 20,000 |
| Blankets, mesh | 4 |  |  | 4 | 3 |  |  |  |  | 17,000 |
| Blankets, mesh (jute) | 1 |  |  | 1 | 1 |  | 20 |  |  |  |
| Blankets, netting | 3 |  |  | 3 | 3 |  |  |  | 2,500 | 6,000 |
| Blankets, netting (jute) | 11 | 1 | 2 | 13 | 8 |  | 110 | 3,600 |  | 107,675 |
| Blankets, polypropylene and coconut fiber | 1 |  |  | 1 | 1 |  |  |  |  | 9,000 |
| Blankets, straw | 8 | 3 | 3 | 14 | 12 | 5 | 5,235 |  |  | 1,121,800 |
| Blankets, straw and coconut fiber | 3 | 4 | 4 | 11 | 9 | 10 | 100 |  | 500 | 1,777,560 |
| Blankets, straw, jute and wood fiber |  | 1 |  | 1 | 1 |  |  |  |  | 300,000 |
| Blankets, synthetic |  | 1 |  | 1 | 0 |  |  |  |  |  |
| Blankets, wood and corn fiber | 1 |  |  | 1 | 1 |  |  |  |  | 750,000 |
| Blankets, wood fiber | 2 |  |  | 2 | 2 |  | 7 |  |  |  |
| Total |  |  |  |  | 70 unique users | 43 | 6,052 | 5,100 | 16,710 | 9,710,415 (=223 acres) |

C=contractor, IECA = International Erosion Control Association, ECS = Erosion control specialist

Table 7. Number of users and quantities of different dust suppressants used in California in 2002.

| Product Type: Dust Suppressant | Number of Users | Number of Users Reporting Amount | Amount |
| --- | --- | --- | --- |
|  | C | IECA | ECS | Total |  | Tons | Gallons | Miles of Road |
| Dust suppressant (unspecified) | 3 |  |  | 3 | 3 | 40 | 17,000 |  |
| Dust suppressant, lignin sulfonate |  |  | 2 | 2 | 2 |  | 1,800 | 10-20 |
| Dust suppressant, magnesium chloride | 2 |  | 1 | 3 | 3 | 25 | 75,000 |  |
| Dust suppressant, water | 24 |  | 2 | 26 |  |  |  |  |
| Total dust suppressant users | 34 |  |

Table 8. Number of users and quantities of lime & fly ash used in California in 2002.

| Product Type: Lime & Fly Ash | Number of Users | Number of Users Reporting Amount | Amount |
| --- | --- | --- | --- |
|  | C | IECA | ECS | Total |  | Tons | Acres | Sacks | Cubic Yards | Square Feet |
| Lime | 19 | 1 |  | 20 | 16 | 3,540 | 27 | 500-1,000 | 120 | 183,900 |
| Fly ash | 3 |  |  | 3 | 3 | 1 |  |  | 20 | 54,000 |

This table does not include one contractor who describes his lime use as “lots”; however, this information is included in the Access Survey Data table.

Table 9. Number of users and quantities of different mulch and fiber materials used in California in 2002.

| Product Type: Mulch & Fibers | Number of Users | Number of Users Reporting Amount | Amount |
| --- | --- | --- | --- |
|  | C | IECA | ECS | Total |  | Acres | Tons | Gallons | Bales | C. Yards | Sq. Feet |
| Bonded fiber matrix | 14 | 4 | 3 | 21 | 17 | 870 | 139 | 200 |  |  | 2,640,000 |
| Mulch (unspecified) | 20 | 4 | 3 | 27 | 22 | 150 | 603 |  |  | 31,210 | 3,845,000 |
| Mulch, paper | 1 |  | 2 | 3 | 2 |  | 124 |  |  |  |  |
| Mulch, recycled green waste | 1 |  |  | 1 | 0 |  |  |  |  |  |  |
| Mulch, sawdust |  |  | 1 | 1 | 1 |  | 15 |  |  |  |  |
| Mulch, stable waste |  |  | 1 | 1 | 1 |  | 5 |  |  |  |  |
| Mulch, straw | 6 | 6 | 12 | 24 | 19 | 500 | 1,093 |  | 1,317 |  |  |
| Mulch, straw (with tack) | 3 |  |  | 3 | 1 |  |  |  |  |  | 1,350,000 |
| Mulch, wood and polyester fiber |  |  | 1 | 1 | 1 |  | 25 |  |  |  |  |
| Mulch, wood chips | 2 | 1 | 5 | 8 | 5 |  | 98 |  |  | 600 |  |
| Mulch, wood fiber | 10 |  |  | 10 | 6 |  | 31 |  |  |  | 6,552,840 |
| Mulch, wood fiber (with guar) |  | 1 |  | 1 | 1 | 23 |  |  |  |  |  |
| Mulch, yard waste | 1 |  |  | 1 | 0 |  |  |  |  |  |  |
| Total |  |  |  |  | 59 unique users | 1,543 | 2,133 | 200 | 1,317 | 31,810 | 14,387,840 (=330 acres) |

Table 10. Number of users and quantities of different soil binders and tackifiers used in California in 2002.

| Product Type: Binders & Tackifiers | Number of Users | Number of Users Reporting Amount | Amount |
| --- | --- | --- | --- |
|  | C | IECA | ECS | Total |  | Acres | Tons | Road Miles | Gallons | Square Feet |
| Soil binder (unspecified) | 5 | 1 |  | 6 | 4 | 70 |  |  |  | 302,840 |
| Soil binder, lignosulfonate |  |  | 1 | 1 | 1 |  | 176 |  |  |  |
| Soil binder, polymer | 5 | 1 | 3 | 9 | 8 | 200 |  | 25 | 4,125 | 1,100,000 |
| Soil binder, tall oil |  | 1 |  | 1 | 1 |  |  |  | 75,000 |  |
| Tackifier (unspecified) | 7 | 1 |  | 8 | 8 | 1,515 | 2 |  |  | 1,312,500 |
| Tackifier, petroleum distillate | 5 | 2 | 1 | 8 | 5 |  |  |  | 4,525 | 2,000,000 |
| Tackifier, plant product | 5 | 7 | 7 | 19 | 13 | 100 | 80 |  |  | 5,500,000 |
| Tackifier, polyacrylamide | 3 | 1 |  | 4 | 3 |  |  |  |  | 7,747,900 |
| Tackifier, polymer | 3 | 1 |  | 4 | 3 |  |  |  | 34,070 |  |
| Total |  |  |  |  | 35 unique users | 1,885 | 258 | 25 | 117,720 | 17,963,240 (=412 acres) |

Table 11. Number of users and quantities of different wattles used in California in 2002.

| Product Type: Wattles | Number of Users | Number of Users Reporting Amount | Amount |
| --- | --- | --- | --- |
|  | C | IECA | ECS | Total |  | Pallets | Rolls | Tons | Linear Feet |
| Wattles (unspecified) | 52 | 6 | 6 | 64 | 56 | 3 | 3,712 | 10 | 927,710 |
| Wattles, coir | 1 |  | 2 | 3 | 3 |  | 80 |  | 400 |
| Wattles, fiber | 4 | 1 |  | 5 | 4 |  |  | 1 | 213,850 |
| Wattles, straw | 30 | 10 | 12 | 52 | 42 | 24 | 17,213 |  | 302,075 |
| Wattles, straw and coir |  |  | 1 | 1 | 0 |  |  |  |  |
| Total |  |  |  |  | 104 unique users | 27 | 21,005 | 11 | 1,444,035 |

This table does not include one contractor who describes his straw wattle use as “lots”; however, this information is included in the Access Survey Data table.

Table 12. Number of users and quantities of different miscellaneous materials used in California in 2002.

| Product Type: Miscellaneous | Number of Users | Number of Users Reporting Amount | Amount |
| --- | --- | --- | --- |
|  | C | IECA | ECS | Total |  | Tons | # Count | Gallons | Linear feet | Square feet |
| Asphalt emulsion, SS1-H | 1 |  |  | 1 | 1 |  |  | 2,400 | 2,400 |  |
| Gravel bags | 4 |  |  | 4 | 3 | 70 | 465 |  |  |  |
| Hay bales | 3 |  |  | 3 | 3 |  | 600 |  |  |  |
| Hydroseed | 4 |  |  | 4 | 3 |  |  | 15,000 | 15,000 | 107,200 |
| Mulch, gravel |  |  | 1 | 1 | 1 | 150 |  |  |  |  |
| Plastic sheeting | 2 |  |  | 2 | 2 |  |  |  |  | 120,000 |
| Sand bags | 2 |  |  | 2 | 2 |  | 3,000 |  |  |  |
| Silt Fence | 11 | 1 |  | 12 | 10 | 1 |  |  | 81,550 |  |
| Wattles, rock | 1 |  |  | 1 | 1 |  |  |  | 2,000 |  |

Brand Name Data Summary

Only 37% of the total respondents (58/155) that give specific information provide a brand name. The average was low, in large part because of the poor response rate of the contractors compared to the ECS and IECA returns (Table 13).

Table 13. Number and percent of respondents reporting product brand names.

| Survey | Respondents with Specific Data | Brand Name Listed |
| --- | --- | --- |
| Contractor | 114 | 32 (28%) |
| ECS | 23 | 14 (61%) |
| IECA | 18 | 12 (66%) |
| Total | 155 | 58 (38%) |

Thirty-six brands are named in the surveys. All brand names, the number of users and those who report amounts appear in Table 14.  The Access Table called Brand Name Usage contains these data with an additional field for general composition. For more details on composition and chemicals of these products, see Tables 15 (Liquids & Powders), 16 (Mulch & Fibers), and 17 (Blankets). Mention of the brand names or lack of mention does not imply any recommendation or lack of recommendation by the State, the University or the authors of this report.

Table 14. Brand Name Use and Amount

| Brand Name | Number of Users | Number of Users Reporting Amount | 2002 Amount |
| --- | --- | --- | --- |
| North American Green | 16 | 13 | 15 acres; 153 rolls; 2,818,800 sq. feet |
| Ecology Controls M-Binder | 15 | 12 | 100 acres; 79 tons; 5,450,000 sq. feet |
| California Straw Works Straw Wattles | 8 | 7 | 76,000 linear feet |
| EarthGuard® | 8 | 5 | 4,525 gallons; 2,000 sq. feet |

Table 14 (continued)

| Brand Name | Number of Users | Number of Users Reporting Amount | 2002 Amount |
| --- | --- | --- | --- |
| EcoAegis® | 7 | 5 | 260+ acres; 200 gallons; 300,000 sq. feet |
| Earth Saver™ | 5 | 4 | 30,600 linear feet |
| UltraTack™ | 4 | 3 | 7,747,900 sq. feet |
| Soil-Sement® | 4 | 4 | 25 miles of road; 100 acres; 2,925 gallons |
| Curlex® | 4 | 4 | 14 rolls; 3,000 linear feet; 300,000 sq. feet |
| Dust-Off® | 3 | 3 | 25 tons; 75,000 gallons |
| Mirafi® | 3 | 3 | 24,500 sq. feet; 8-9 rolls |
| Terra-Lock™ 50 | 3 | 2 | 100+ acres; 100 gallons |
| EcoFibre® | 3 | 1 | 6,550,000 sq. feet |
| Greenfix® Erosion Control Blankets | 3 | 3 | 5,500 rolls; 40,500 sq. feet |
| EcoAegis II® | 3 | 1 | 100 + acres |
| EarthGuard® Fiber Matrix | 2 | 2 | 22 acres |
| Rolanka BioD-Watl™ | 2 | 2 | 280 linear feet |
| Soil Saver™ | 2 | 2 | 1,370,000 sq. feet |
| GEOCOIR®/DeKoWe® | 2 | 2 | 562,500 sq. feet |
| Landlok® Blankets | 2 | 2 | 99,000 sq. feet |
| Envirotac II® Soil Stabilizer | 2 | 1 | 2,000 gallons |
| Conwed Fibres® Hydro Mulch 1000 | 1 | 1 | 25 tons |

Table 14. (continued)

| Brand Name | Number of Users | Number of Users Reporting Amount | 2002 Amount |
| --- | --- | --- | --- |
| Conwed Fibers® 3000 | 1 | 1 | 25 tons |
| Conwed Fibers® 2000 | 1 | 1 | 1 ton |
| BonTerra CS2™ | 1 | 1 | 2,880 sq. feet |
| TOPEIN™S | 1 | 1 | 75,000 gallons |
| Soil Master WR | 1 | 1 | 14,520 gallons |
| Dustac® 100 | 1 | 1 | 176 tons |
| Landlok® BioLog® | 1 | 1 | 200 linear feet |
| Landlok® Turf Reinforcement Mat | 1 | 0 |  |
| Mat Grass-Mat™ | 1 | 1 | 750,000 sq. feet |
| NaturesOwn Mulch | 1 | 1 | 7,000 lbs. |
| Soil Guard™ | 1 | 1 | 500 + acres |
| PolyPavement™ | 1 | 1 | 1,100 gallons |
| Pyramat® | 1 | 0 |  |
| EarthWorks Gorilla Hair | 1 | 1 | 1 ton |

Table 15. Brand Composition: Liquids & Powders.

| Brand Name | General Composition | MSDS Chemicals |
| --- | --- | --- |
| Dustac® 100 | calcium lignosulfonate | calcium lignosulfonate |
| Dust-Off® | magnesium chloride, magnesium sulfate | magnesium sulphate heptahydrate magnesium chloride |
| EarthGuard® | copolymer of acrylamide/sodium acrylate; petroleum distillate (20.5-22.5%), sodium metabisulfite (0.6-0.8%) | distillates (petroleum), hydrotreated light sodium metabisulfite |
| Ecology Controls M-Binder | ground muciloid seed coat | unknown |
| Envirotac II® Soil Stabilizer | acrylic co-polymer (39-43%), residual monomers (<0.1%), ammonia (<1.0%) | ammonium hydroxide |
| PolyPavement™ | vinyl acrylic copolymer (96+%), emulsifier (1+%), surfactant (1+%) | unknown |
| Soil Master WR | polyvinyl acetate | unknown |
| Soil-Sement® | acrylic and vinyl acetate polymer (5-50% by wt) | unknown |
| Terra-Lock™ 50 | sodium acrylate/acrylamide copolymer (50%) dispersed in mineral oil, petroleum distillates (35% by wt), surfactant, impurities include acrylic acid(<0.5% by wt) and acrylamide (<0.10% by wt) | acrylamide/sodium acrylate polymer sorbitan oleate distillates (petroleum), hydrotreated light naphthenic |

Table 15. (continued)

| Brand Name | General Composition | MSDS Chemicals |
| --- | --- | --- |
| TOPEIN™S | tall oil by product (42-48% by wt), nonylphenol polyethylene glycol ether as surfactant, hydrochloric acid (<1.0%) | unknown |
| UltraTack™ | anionic polyacrylamide, | unknown |

Table 16. Brand Composition: Mulch & Fibers

| Brand Name | General Composition | MSDS Chemicals |
| --- | --- | --- |
| Conwed Fibers® 2000 | wood fiber, guar gum | guar gum |
| Conwed Fibers® 3000 | wood fiber, polyester fiber | guar gum |
| Conwed Fibres® Hydro Mulch 1000 | wood fiber, green dye | unknown |
| EarthGuard® Fiber Matrix | copolymer of acrylamide/sodium acrylate; petroleum distillate (20.5-22.5%), sodium metabisulfite (0.6-0.8%), wood/cellulose fiber | distillates (petroleum), hydrotreated light sodium metabisulfite |
| EarthWorks Gorilla Hair | recycled redwood | unknown |
| EcoAegis II® | softwood fiber, guar gum (<10%), green dye | guar gum |
| EcoAegis® | softwood fiber, guar gum (<10%) | guar gum |
| EcoFibre® | wood fiber, green dye (<0.1%) | C.I. Basic Green 4, oxalate |
| NaturesOwn Mulch | wood fiber | unknown |
| Soil Guard™ | wood fiber, guar, polysaccharide, methine dye | unknown |

Table 17. Brand Composition: Blankets.

| Brand Name | General Composition |
| --- | --- |
| North American Green | straw, coconut or mixed fiber |
| Curlex® | various |
| Greenfix® Erosion Control Blankets | straw or coir fiber, polypropylene netting |
| Mirafi® | various |
| Soil Saver™ | jute |
| Landlok® Blankets | various |
| GEOCOIR®/DeKoWe® | coir fiber |
| Pyramat® | polypropylene |
| Mat Grass-Mat™ | wood and corn fiber, rayon netting |
| Landlok® Turf Reinforcement Mat | polyolefin fiber, polypropylene netting |
| BonTerra CS2™ | straw, coir, polypropylene |

Application Rate Data

Application rate data for contractors and manufacturers, pertaining to the survey is contained in the Access Survey Data table. Twenty-eight respondents provide application rate information for 50 products. Of these respondents, 20 gave application rate information for 21 products with brand names (see Table 18). When brand names are provided, the contractor application rate can be compared to manufacturer recommended rates.  Eight of the 21 products (40%) listed in Table 18 were applied in excess of the manufacturer’s recommended application rate: EarthGuard® (3 instances), EcoAegisII® (1 instance), Ecology Controls M-Binder (2 instances), EnvirotacII® (1 instance), and Soil Master WR (1 instance). In addition, three had possible excess application rates.

Those items with application rates and no brand name include a variety of materials: bonded fiber matrix, mulch, soil binder and tackifier. In the mulch category, twelve respondents reported application rates ranging from 1.5 to 2 tons per acre for straw mulch, three wood-fiber mulch users reported rates ranging from 0.75 to 1.5 tons per acre, and one stable waste mulch user applied 10 tons per acre. We have insufficient data to make conclusions about the appropriate rates of use of materials. Use of materials in excess of manufacturer’s recommendations may be based on the user’s experience with the materials or with the general concept that if a small amount is good, more is better.  In the vast majority of cases, in which no known toxicity exists, excess use of materials is not bad but may have a negative impact on the cost of erosion and dust control.

Table 18. Comparison of contractor application rate to manufacturer recommended application rate based on survey responses.

| Brand Name | Amount Used in 2002 | Contractor Application Rate | Manufacturer Application Rate | Excess |
| --- | --- | --- | --- | --- |
| EarthGuard® | 200 gallons | 8 gallons/acre | 2-5, 2-8, or 4-10 gallons/acre depending on use | Possibly |
| EarthGuard® |  | 8 gallons/acre | 2-5, 2-8, or 4-10 gallons/acre depending on use | Possibly |
| EarthGuard® |  | 6-8 gallons/acre | 2-5, 2-8, or 4-10 gallons/acre depending on use | Possibly |
| EcoAegis II® |  | 3,500 lbs./acre | Depending upon slope, soil and weather, apply 2700 to 3500 lbs./acre. | No |
| EcoAegis II® | 100 + acres | 3,500 to 4,000 lbs./acre | Depending upon slope, soil and weather, apply 2700 to 3500 lbs./acre. | Yes |
| EcoAegis® |  | 2,000-3,000 lbs./acre | 3500 to 4100 lbs./acre | No |
| EcoAegis® | 60 acres | 3,500-4,200 lbs./acre | 3500 to 4100 lbs./acre | Possibly |
| EcoAegis® | 100 + acres | 3,500 to 4,000 lbs./acre | Depending upon slope, soil and weather, apply 3500 to 4100 lbs./acre. | No |
| EcoFibre® |  | 1,500-3,000 lbs./acre | 1800 to 2000 lbs./acre | Possibly |
| Ecology Controls M-Binder | 10,000 lbs. | 80-150 lbs./acre | 40 to 160 lbs./acre. | No |
| Ecology Controls M-Binder |  | 250 lbs./acre | 40 to 160 lbs./acre | Yes |
| Ecology Controls M-Binder | 100 acres | 130 lbs./acre | 40 to 160 lbs./acre | No |
| Ecology Controls M-Binder | 30 tons | 150 lbs./acre | 40 to 160 lbs./acre | No |
| Ecology Controls M-Binder | 300 lbs. | 175 lbs./acre | 40 to 160 lbs./acre | Yes |

Table 18. (continued)

| Brand Name | Amount Used in 2002 | Contractor Application Rate | Manufacturer Application Rate | Excess |
| --- | --- | --- | --- | --- |
| Ecology Controls M-Binder | 50,000 lbs. | 120-200 lbs./acre | 40 to 160 lbs./acre | Possibly |
| Envirotac II® Soil Stabilizer |  | 300 gallons tackifier + 400 lbs. mulch + 1,000 gallons water per 1.5 acre | 109 to 113 gallons/acre | Yes |
| Hydro Mulch (Conwed, unspecified) |  | 2 tons/acre | 1,500 to 4,000 lbs./acre | No |
| Soil Master WR | 14,520 gallons | 165 gallons/acre | 55-110 gallons/acre | Yes |
| Terra-Lock™ 50 |  | 6-8 gallons/acre | 1-10 gallons/acre | No |
| TOPEIN™S | 75,000 gallons | 550 gallons/acre | Dilute 1:1 to 1:12 depending upon use. Apply 0.20 to 1.2 gallons of dilution/square yard. | No |
| UltraTack™ |  | 5 lbs./acre | 3-5 lbs./acre | No |

Comments

A number of the respondents include comments about the materials they use. Table 19 is organized by product type. When mentioned by the respondent, the brand name is included. Most respondents are happy with the materials they are using.

Table 19. Survey comments made by survey respondents.

| Product Type | Brand Name | Respondent Comments |
| --- | --- | --- |
| Asphalt emulsion, SS-1H |  | Used to stick new asphalt to existing asphalt. |
| Blankets (unspecified) | Curlex | Curlex is a fantastic product needing little to no maintenance. |
|  | North American Green | Efficacy: good Subject to rilling and tenting, contractor does not like. Efficacy: good |

Table 19. (continued)

| Product Type | Brand Name | Respondent Comments |
| --- | --- | --- |
| Blankets, coconut fiber | GEOCOIR®/DeKoWe® | For slope erosion stabilization with no hydroseeding, tough to maintain proper surface contact. |
|  | Greenfix® Erosion Control Blankets | We use different brands in different situations based on roll size, price and availability. |
|  | North American Green C125 | Post hydroseeding, easy to apply with DOT system and proper staples. |
| Blankets, excelsior or straw |  | Too expensive, not very effective, used mostly in small areas where it is cost effective. |
| Blankets, geotextile | Landlok® Turf Reinforcement Mat | Used to stabilize drainage ditches that required permanent vegetation. |
|  | Pyramat® | Used to stabilize 1 x 3 foot berms in retention pond. Expensive product. |
| Blankets, netting (jute) |  | Best product: seeding with rye grass. Not effective Jute netting is less effective on cobbly, colluvial soils because net-soil contact is difficult to maintain. |
| Blankets, straw | North American Green S75 | Post hydroseeding, easy to apply with DOT system and proper staples. |
|  | North American Green S150 | Post hydroseeding, easy to apply with DOT system and proper staples. Efficacy: good |
|  | Greenfix® | Works well |
| Blankets, straw and coconut fiber | North American Green SC150 | Efficacy: excellent Post hydroseeding, easy to apply with DOT system and proper staples. Efficacy: good |
| Blankets, straw, jute and wood | Curlex | Efficacy: excellent |

Table 19. (continued)

| Product Type | Brand Name | Respondent Comments |
| --- | --- | --- |
| Bonded fiber matrix |  | Efficacy: excellent |
|  | EcoAegis® | Used as temporary stabilization for permanent vegetation. Efficacy: 90-95% for 9-12 months. |
|  | EcoAegis II® | Efficacy: excellent Used as temporary stabilization for permanent vegetation. Efficacy: 90-95% for 6-9 months |
|  | Conwed Fibres® | Efficacy: good |
| Dust suppressant, magnesium chloride | Dust-Off® | Magnesium chloride tends to break down very quickly when there are organics on the roads(wood chips) and generally works much better on normal roads when the first full application is followed up four weeks later with a lighter application. Magnesium chloride deteriorates quickly with overuse and requires maintenance (light watering) to maintain its integrity. |
| Dust suppressant, water |  | Applied daily Used as needed for small offsite construction and fly ash disposal areas. |
| Gravel bags |  | Bags need to be placed tightly together to hold the fines from the soils back. The bags rot in then sunlight over time and are usually damaged by trucks and equipment on job sites as the workers are not careful around them. |
| Lime |  | Efficacy: works well |
| Mulch |  | Mulch is site generated clipped native cover. |
|  | Hydro Mulch (Conwed, unspecified) | Efficacy: good Efficacy: excellent Efficacy: good |

Table 19. (continued)

| Product Type | Brand Name | Respondent Comments |
| --- | --- | --- |
| Mulch, paper |  | For stronger applications, we combine the polymer with paper mulch to assist as a binder. This application is very effective. The only product that works better is some sort of ground cover. The polymer alone works better on soils containing higher contents of silts and clays. The paper mulch mix works better for the sandier soils but also works universally. The supplier uses this product all over southern California. |
| Mulch, stable waste |  | Typically, the sawdust and stable waste are spread and disked, then covered with straw mulch after reseeding. |
| Mulch, straw |  | Efficacy: excellent Straw mulch needs to be crimped or trackwalked in windy situations. Crimping may allow for somewhat lighter applications. Heavier applications (more than 2 tons/acre) may inhibit cover crop germination and growth. |
| Mulch, straw (native) |  | We try to use native mulch similar to the seed we are using. Elymus glaucus or fescues are my favorites. |
| Mulch, straw (rice) |  | Excellent Most cost effective mulch. |
| Mulch, straw (with tack) |  | Straw with tack is a standard for us – in that it is reasonably priced. It can be blended in with the soil and it seems to work the best. |
| Mulch, wood chips |  | Excellent erosion control, controls weeds, encourages natives. |
| Mulch, wood fiber (with guar) |  | Efficacy: 80-85% for 3-6 months |
| Plastic sheeting | Visqueen | Used to cover stockpiles. |
| Silt fence |  | Efficacy: good |
| Soil binder (unspecified) |  | Efficacy: good |

Table 19. (continued)

| Product Type | Brand Name | Respondent Comments |
| --- | --- | --- |
| Soil binder, polymer | Soil-Sement® | Used as dust suppressant on road. Dust control |
| Soil binder, tall oil | TOPEIN™S | Efficacy: excellent |
| Soil stabilizer | EarthGuard® | Efficacy: excellent Efficacy: excellent |
| Tackifier, plant product | Ecology Controls M-Binder | Good for temporary control Good for locking straw Used for tacking straw and wood fiber mulches. Efficacy: good Efficacy: good Efficacy: excellent Used for hydroseeding stream banks. Used on straw Efficacy: excellent |
| Tackifier, plant product (guar) |  | Applied over straw |
| Tackifier, polyacrylamide | UltraTack™ | Works for 3 to 1 slope I like a hydroseed mix with tack, that way you get more immediate and long-term protection. A tack with dye is cheap and looks pleasing to city inspectors. The more application, the better the performance, usually. |

Table 19. (continued)

| Product Type | Brand Name | Respondent Comments |
| --- | --- | --- |
| Tackifier, polymer | Soil Master WR | Good for temporary control |
|  | Envirotac II® Soil Stabilizer | Dust control For stronger applications, we combine the polymer with paper mulch to assist as a binder. This application is very effective. The only product that works better is some sort of ground cover. The polymer alone works better on soils containing higher contents of silts and clays. The paper mulch mix works better for the sandier soils but also works universally. The supplier uses this product all over southern California. |
| Wattles |  | Efficacy: good Better than silt fence Efficacy: good Efficacy: excellent Used in areas where water would be running. Views on all erosion control products: you typically need to adjust recommended application rates and add more after the first rain. |
| Wattles, coir | Rolanka BioD-Watl™ | Used on slopes to slow the flow of water and as filters around drains. They hold up better than the bags of sand and gravel and take less effort. One wattle can replace three bags. I like wattles because they are easier to handle and take less storage space than piles of sand or gravel. They also take less manpower to distribute and are more visually appealing to the public and inspectors, however they are definitely more costly. Used for stream bank toe protection. |

Table 19. (continued)

| Product Type | Brand Name | Respondent Comments |
| --- | --- | --- |
| Wattles, fiber |  | Efficacy: good |
| Wattles, straw |  | Efficacy: great Works well but not perfect Used on upper slopes as water breaks and as seed collection basins. Worked well |
|  | Earth Saver™ | Efficacy: excellent Excellent |
|  | California Straw Works Straw Wattles | Difficult to apply in rocky soils Efficacy: good Used on relatively flat surfaces and as check dams. Performed well on clayey soils and are less of a maintenance headache than silt fences. Efficacy: excellent |

Task 3.  Perform a background search and if appropriate and feasible reanalyze data generated by other research efforts on storm water impacts from construction materials.

To better understand storm water impacts from construction materials, we performed a background literature search on this topic and organized the data into the Access Pollutants (building materials) Table. Building material pollutant information comes from storm water runoff and laboratory leachate research found in the following databases: TOXLINE, Environmental Engineering Abstracts, TRIS Online, Civil Engineering Database (ASCE), Water Resources Abstracts, Pollution Abstracts, ASFA 3: Aquatic Pollution and Environmental Quality, Web of Science, Dissertation Abstracts,  and Conference Papers Index. The 68 studies, published between 1978 and 2004, with data on 117 materials, are contained in the Access Pollutant Table in the appendix and on the web site. An example of the information in the Access table is shown in table 20.

The Pollutant Table lists pollutants that may leach from actual and potential generic building materials. The data are organized into 6 fields: material, type, use, pollutant/constituent, water source, and reference. In addition, the materials are categorized by type: building material (89 items), erosion control materials (10 items), pesticides (4 items), miscellaneous (3 items), and construction and demolition waste (11 items), which includes materials created from construction and demolition waste and the waste itself. Because most of the erosion control material solubility and toxicity data appear in other Access tables, those listed in the Pollutant Table are generic materials.

Table: 20 Building Material Pollutants

| Material | Category | Use | Constituent | Water source | Study reference |
| --- | --- | --- | --- | --- | --- |
| Resins | construction & demolition waste |  | isocyanates, phothalic, anhydride | leachate | Symonds (1999) |
| Oils & fuels | construction & demolition waste |  | hydrocarbons | leachate | Symonds (1999) |
| Fly ash | construction & demolition waste | sub base waste | heavy metals | leachate | Symonds (1999) |
| Wood preservatives pentachlorphenol | building material |  | dioxins, furans | storm water | Fisher (1999) |
| Roofing components, zinc | building material |  | zinc | storm water | Karlen (2001) |
| Termiticide | pesticide |  | chlorpyrifos | storm water | Carr (1997) |
| roofing | building material |  | zinc | storm water | Pitt (2000) |
| Wood preservatives | building material |  | copper, chromium, arsenic, pentachlorophenols | storm water | Pitt (2000) |
| Wood preservatives, creosote | building material |  | PAHs | storm water | Pitt (2000) |
| Wood preservatives, CCA | building material |  | copper, arsenic, chromium | leachate | Hingston (1999) |
| Roofing, zinc | building material |  | zinc, cadmium | storm water | Gromaire (2001) |
| Pipe, PVC | building material |  | organotin compounds | tap water | Sadiki (1996) |
| Herbicide | pesticide | roof sealant | (R,S)-mecoprop | storm water | Bucheli (1998) |
| Roofing, galvanized | building material |  | zinc | storm water | Sorme (2002) |
| Roofing, copper | building material |  | copper | storm water | Sorme (2002) |
| Gasoline | building material |  | hydrophobic VOCs | storm water | Lopes (2000) |

Table 20. (continued)

| Material | Category | Use | Constituent | Water source | Study reference |
| --- | --- | --- | --- | --- | --- |
| Wood preservatives, ACZA | building material |  | arsenic, copper, zinc | leachate | Eldin (2002) |
| asphalt cement concrete, MSW ash | building material | road building | aluminum | leachate | Eldin (2002) |
| Portland cement concrete, with plasticizer | building material | road building | aluminum, calcium | leachate | Eldin (2002) |

Building Materials, the largest category, includes concrete, aggregate, adhesive, solder, road building materials, roofing materials and components, siding, treated wood, paint, pipe, sealer, plasticizer, coating, and unconfined combustion wastes. The smaller Erosion Control category contains mulch, blankets, bonded fiber matrix, tackifier, wheat straw and aspen wood chips. Construction and demolition waste as a whole, specific waste from construction, such as resin, oil and fuel, and materials made from the waste, such as aggregate and concrete, are found in the Construction and Demolition Waste category. The Pesticides category includes herbicides and insecticides that are associated with construction sites or building materials. A few items such as road salt and road degradation dust are placed in the miscellaneous category.

The Use field applies to those materials in loose form that may have a variety of applications, such as fly ash, some of which include the following: road building, embankments, soil stabilizer, and backfill.

Most of the research reported in the Pollutant Table examined pollutants and constituents in storm water runoff or in laboratory leachate studies, therefore the Water Source field will usually show Storm Water (47 instances) or Leachate (57 instances).  This table also includes a few studies on tap water, ground water and drain water relevant to building materials.

The majority of research examines the presence of metals in runoff or leachate, therefore most of the pollutants listed are metals such as copper, zinc, cadmium, chromium, cyanide, aluminum, iron, silver, molybdenum, lead, boron, nickel, antimony, and vanadium. Other items found in runoff and leachate from these investigations include PAHs, VOCs, organo-tin compounds, phthalates, pentachlorophenols, dioxins, furans, sulfate, bitumens, nitrate, phosphate, increased TOC, COD and TDS, and high pH. One study found aspen wood chip leachate (1% undiluted leachate) acutely toxic to trout. Six blankets listed in the Access product table use aspen fiber.

In the Miscellaneous category, we added road degradation dust, which can range from 1,734 to 11,000 kg/ha of road per year, depending upon road type (Munkshack, 1990). Although it is not a construction site issue, the degraded road paving material, whether particulate or soluble, will end up in storm water. A look at the items in the Pollutant Table with road building in the Use field may give a general idea of a few of the constituents in road degradation dust that may wash off with storm water.

The Pollutant table does not address the potential to be leached (leachability). Some materials may have a low concentration of a pollutant yet have high leachability or high concentration and low leachability (van Houdt, 1991). Nevertheless, slow leaching of metals and organics can be an important source of pollutants over the long-term (Lalor, 2003). One study in France found that 50% of zinc found in Paris runoff comes from zinc roofing which makes up 40% of all roofing in Paris (Gromaire, 2001). As construction density increases, so does the pollutant load from these materials (Davis, 2000). Ultimately, the accumulation of material leachate data can help us choose materials with fewer environmental impacts.

An example of potential pollution from an unlikely source is the presence in mulch and tackifiers of a green dye. A number of mulch and tackifier (41 items) materials in the Product List contain green dye for metering when hydroseeding or hydromulching. Most (5 dyes) belong to the triphenylmethane family of basic dyes commonly used in the pulp and paper industry. One mulch product contains C.I. Basic Yellow 96, a paper dye belonging to the methine family. The concentration of dye in mulch is usually 1% or less by weight. Solubility may vary from insoluble to very soluble. All have a strong affinity for fibers, clay, and other particulate materials and are slowly degraded.  In one study on rainbow trout, the extensive sorption of dye on gills and mouths blocked respiration (Milanova 1997). Aquatic toxicology data are contained in the Access table called Green Dye Toxicology as shown below in Table 21. One mulch product with 0.5% by weight of C.I. Basic Green 4 dye with a recommended application rate of 1200 lbs/acre would result in 60 lbs/acre of green dye.

Table 21. Green Dye Water Solubility and Aquatic Toxicology

| Dye Name | CAS No. | Water Solubility | Aquatic Toxicology | Data Source |
| --- | --- | --- | --- | --- |
| C.I. Basic Green 1 | 633-03-4 | 40g/L | LC50/fish/ 96h/ 1-10mg/L | BASF Company MSDS |
|  | 633-03-4 | 40g/L | Resistant to biodegradation. Bioaccumulation in aquatic organisms is low. Has very high mobility in soils. | Hazardous Substances Data Bank (NLM) |
| C.I. Basic Green 4 | 569-64-2 | 50g/L | LC50/fish/ 48h/<1mg/L and LC50/fish/ 66 - 5600µg/L | BASF Company MSDS and PAN Pesticide Database |
|  | 569-64-2 | Very soluble | LC50/96hr/bluegill/ 0.0305mg/L, LC50/96hr/salmon/ 0.338mg/L, LC50/96hr/rainbow trout/0.0998mg/L, LC50/96hr/frog/0.173mg/L, LC50/96hr/asiatic clam/122mg/L, LC50/96hr/mayfly naiad/0.0790mg/L, LC50/96hr/eel /0.25mg/L, LC50/24hr/fingerling channel catfish/0.14ppm | Hazardous Substances Data Bank (NLM) |

Table 21. (continued)

| Dye Name | CAS No. | Water Solubility | Aquatic Toxicology | Data Source |
| --- | --- | --- | --- | --- |
| C.I. Basic Green 4, oxylate | 18015-76-4 | Slight to insoluble | LC50/fish/ 140-790µg/L | Solubility from Conwed Proplus™ Slikcolor™r MSDS; toxicology from PAN Pesticide Database |
|  |  |  | LC50/rainbow trout/96h/0.39-0.77mg/L | Milanova (1997) |
| Triphenylmethane, unspecified | 519-73-3 | insoluble | No data | Acros Organics N.V. MSDS |
| Triarylmethane, unspecified | none | insoluble | LC50/fish/ 96h/ 0.1-1mg/L | BASF Company MSDS |
| C.I. Basic Yellow 96 (Basazol Yellow 46L) | 16793-11-7 | miscible | EC50/Microtox/ 15min/10.7mg/L | Solubility from BASF MSDS; toxicology from Milanova (1997) |

Task 4.  Determine what current good housekeeping best management practices are used in the construction industry.

Soil disturbance during construction is a widely known part of the land development process that can lead to a significant increase in erosion and the need for sediment control throughout the duration of construction.  Erosion is a three-step process involving detachment, transportation, and deposition of soil particles.  Erosion rates from construction sites have been measured to be 2 to 40,000 times greater than before ground disturbance (Wolman and Schick 1967).  Excavation and vehicular movement during construction activities dramatically increase soil erosion rates and become a major contributor to non-point source pollution (NPS) (Herzog et al. 2000).

Sediment resulting from construction has been identified as one of the foremost non-point source pollutants of our waterways.  The reduction of sediment has become an important aspect of construction planning and has contributed to the creation of a large number of erosion and sediment control materials (See Task 1 results).  Best management practices (BMPs) are a combination of structural, vegetative, and management practices to reduce sediment pollution.  Sediment loads into watersheds are inherently variable and site dependent (Daniel et al. 1979).  Surface runoff from construction sites carries suspended solids that may pollute water and damage fish and wildlife habitat. Increased sediment loads into water bodies can significantly impact aquatic organisms (Donohue et al. 2003).

We used selected Storm Water Pollution Prevention Plans (SWPPPs) in close proximity to UC Davis to determine what Best Management Practices (BMPs) were being used in California and to determine the efficacy of the plans.  We envisioned a three-part process.  First we selected plans and examined them to determine if they were adequate.  Second, we would inspect each site to determine if the plans had been implemented properly and third, we would continue inspections throughout the rainy season to determine if the implemented plans were effective.  At the time we initiated this, we also expected to sample storm water runoff, but this was not done during 2003-2004.

For part 1, we randomly selected 75 Storm Water Pollution Prevention Plans (SWPPPs) over 5 acres from Placer, El Dorado and Sacramento counties from the SWPPP applicant database on the State Water Resources Control Board website. We selected these three counties because of the rapid growth of a wide range of construction activities in various stages of construction of residential and commercial buildings and their proximity to Davis. The terrain within the counties ranges from primarily flat in Sacramento County to steep slopes in El Dorado County.  The implementation of Best Management Practices (BMPs) and compliance with the SWRCB General Permit were evaluated in this study. To insure that the selection was random, 3 sub-tables containing sites with active permits were created from the SWPPP database and given random numbers by the Access program. We chose the first 25 random records for each county. Individual site SWPPPs were requested on October 29, 2003 (Appendix 3) through the RWQCB. The letter, mailed to the landowner listed with the associated WDID number, requested that the SWPPP be mailed to the RWQCB office 10 days from the date of the letter, (October 24, 2003).

Prior to the SWPPPs submission, a checklist with a scoring system was made to rank the perceived effectiveness of the SWPPP so that field visits could be made to qualitatively determine if the use of BMPs throughout the selected sites was correct (Appendix 2, Table 22).  In order to make the checklist the Erosion and Sediment Control Field Manual by the California Regional Water Quality Control Board, San Francisco Bay Region was used to produce field guidelines.  Two meetings were conducted to determine the possible efficacy of the checklist.  The first meeting was with Dr. Michael Singer, Libby Raskin and Angela De Paoli and produced a need for a rating system within the checklist for the first review of the SWPPP and the field visits.  The second meeting was with Libby Raskin, Angela De Paoli, Kathleen Groody, Richard Muhl, Dannas Berchtold and one other RWQCB inspector.  During this meeting the checklist was refined to include the expertise of the RWQCB inspectors.

We determined that the most important component of a high quality SWPPP was site specificity.  This is reflected in the ranking system in Table 22. SWPPPs with direction on BMP locations and types of materials were given higher scores, whereas sites with little to no site specificity were given lower scores.

Table 22. SWPPP Scoring System

| Grade | Definition |
| --- | --- |
| 5 | Excellent=Site specific, BMP locations given in map and text, highly site specific |
| 4 | Good=Map provides good information on BMP locations, little to no information in the body of the text, some BMPs left to the contractor to determine, site specific |
| 3 | Average=General BMPs listed, information given is on general waste controls and BMP maintenance, few to no specific recommendations, moderately site specific |
| 2 | Below Average=General BMPs listed, little to no site specific BMPs given in text or on map, partially site specific |
| 1 | Poor=No body of text and/or no site map provided, no BMP types are listed or recommended, not site specific |

An 80% return rate of the SWPPPs to the RWQCB was expected.  The final response rate was <50% (Table 23).  The Active SWPPPs are those SWPPPs that were currently under construction during the inspection period over the winter of 2003-2004. Terminated SWPPPs are those that were submitted to the RWQCB in response to our letter, but the landowner stated construction was completed. The letters column includes letters that were mailed to the RWQCB stating the project is complete and the final column includes the request letters that were undeliverable due to a bad address.

Section 308(b) of the Clean Water Act, requires that the SWPPP “shall be provided, upon request” to the RWQCB for public access (SWRCB 1999).  Although required by law, many of the requested SWPPPs were not available for review.  The Regional Board received many reasons from landowners as to why the SWPPPs were not supplied.  Some of the comments on why SWPPPs were not sent to the Regional Board are : 1) who is requesting the information and why?  2) Would provide the information but only if the land owner knew the name of the party requesting the SWPPP. 3) Many of the people who the requests went to were worried about third party lawsuits.  4) Job has been completed.5) Property has been sold to someone else.  Because there is no time constraint on when SWPPPs must be provided to the RWQCB, many SWPPPs were not received by the time this study began (30 days after the letter was sent).

Table 23. Classification of responses to the request for SWPPPs.

| County | No response | Active SWPPP | Terminated SWPPPs | Letters stating project is complete | Undeliverable Address |
| --- | --- | --- | --- | --- | --- |
| Placer | 13 | 9 | 1 | 0 | 2 |
| Sacramento | 14 | 7 | 1 | 1 | 2 |
| El Dorado | 6 | 16 | 0 | 2 | 1 |
| Total | 33 | 32 | 2 | 3 | 5 |

All 32 active SWPPPs were reviewed. They represented a wide range of quality (Tables 24, 24a).  The SWPPP content and construction site visit data are contained in the Access table called SWPPP and Construction Site Data (Tables 62A and 62B).

Table 24.  Number of SWPPPs by type (residential, commercial or other), designer, and quality of individual SWPPPs according to the criteria in Table 23.

| Number of SWPPPs Examined | Average Acreage | Number of SWPPPs by Type | Number of SWPPPs by Designer Type | Number of SWPPPs by Quality |
| --- | --- | --- | --- | --- |
| 32 | 84 | R | C | A | O | Ct | E | Cs | Ow | 1 | 2 | 3 | 4 | 5 |
|  |  | 21 | 5 | 3 | 4 | 1 | 17 | 10 | 4 | 3 | 12 | 9 | 2 | 6 |

R=residential	         Ct=contractor

C=commercial          E=engineer

A=apartment            Cs=consultant

O=other                    Ow=owner

The SWPPPs were written by contractors, engineers, consultants, and individual landowners.  The average score for the 32 SWPPPs received was 2.87, slightly below average.  SWPPP quality was found to be, to a certain extent, related to the designer.  It appeared that consultants wrote the highest scoring plans.  SWPPPs designed by engineers (53%)had 59% of their SWPPPs score below average (Table 24a). The major reason SWPPPs scored below average was that they were only partially site specific, with little or no site specific BMPs given in the text or maps (Table 62A).

Table 24a. SWPPP Quality by Designer Type

| SWPPP Grade | SWPPP Designer Count |
| --- | --- |
|  | Consultant | Contractor | Engineer | Owner |
| 5 | 4 | 0 | 2 | 0 |
| 4 | 0 | 0 | 1 | 1 |
| 3 | 4 | 0 | 4 | 1 |
| 2 | 2 | 0 | 10 | 0 |
| 1 | 0 | 1 | 0 | 2 |

SWPPP preparers most frequently recommended five primary BMPs for erosion and sediment control.  Silt fence and wattles were the most recommended BMPs followed by stabilized construction entrances, gravel bags, mulch, and tackifier (Table 25).

Table 25. Number of each kind of BMP Recommended by SWPPP preparers and number of sites that used the recommended kind of BMP.

| BMP Type | # of SWPPPs Recommending | % of SWPPPs Using | # 0f Active Sites Using | % of Sites Using |
| --- | --- | --- | --- | --- |
| Berm | 3 | 9% |  |  |
| Blankets/geotextiles | 2 | 6% | 4 | 12% |
| Check dams | 5 | 15% |  |  |
| Concrete washout | 1 | 3% | 4 | 12% |
| DI protection | 5 | 15% |  |  |
| Dumpsters |  |  | 2 | 6% |
| Entrance/exit stabilization | 12 | 36% | 1 | 3% |
| Existing vegetation | 2 | 6% | 2 | 6% |
| Filtration, secondary | 1 | 3% |  |  |
| Gravel bags | 8 | 24% | 12 | 36% |
| Hay bales | 3 | 9% | 1 | 3% |
| Hydromulch/bfm | 5 | 15% |  |  |
| Hydroseed | 4 | 12% | 2 | 6% |
| Geotextiles |  |  |  |  |
| Mulch, straw | 8 | 24% | 3 | 9% |
| Sediment basin | 1 | 3% | 1 | 3% |
| Sediment trap | 4 | 12% |  |  |
| Silt fence | 15 | 45% | 2 | 6% |
| Staging area | 8 | 24% |  |  |

Table 25. (continued)

| BMP Type | # of SWPPPs Recommending | % of SWPPPs Using | # 0f Active Sites Using | % of Sites Using |
| --- | --- | --- | --- | --- |
| Street sweeping | 1 | 3% |  |  |
| Tackifier | 8 | 24% | 4 | 12% |
| Tire wash |  |  | 1 | 3% |
| Track walking | 3 | 9% |  |  |
| Wattles | 21 | 64% | 11 | 33% |
| Silt sacs | 3 | 9% | 5 | 15% |
| Secondary filtration | 1 | 3% | 2 | 6% |
| Winterized stockpiles | 1 | 3% |  |  |
| Housekeeping | 1 | 3% |  |  |

Site visits helped determine what BMPs were currently being used and if they reflected the recommendations of the SWPPPs. Correlations between SWPPPs and current site conditions could often not be made due to various factors, including that construction was complete, and the current construction phase did not match the phase on the SWPPP.  Perhaps most important was that most SWPPPs were not site specific enough to relate them to the site condition.

Site visits revealed that BMPs, such as wattles, gravel bags and silt sacs recommended in the SWPPPs were used frequentlyon-site and that most of the remaining recommendations were used much less frequently.  During the site visits, 50% of the sites were found with construction complete (Table 26).  In addition, due to variations in construction phasing, the BMPs that were found in use may have been due to current site conditions and not based on recommendations made in the SWPPP.

Table 26. Number of sites visited and the stage of construction of each active site.

| Number of Sites Visited | Number of Sites Completed | Number of Non-Active Sites | Number of Active Sites in Each Phase | Number of Active Sites with BMPs |
| --- | --- | --- | --- | --- |
| 32 | 15 | 1 | Grading | Production | Landscaping | 16 |
|  |  |  | 4 | 11 | 1 |  |

Of the BMPs used on-site,10 BMPs and sediment control issues were found out of compliance with the General Permit (SWRCB 1999).   Items most often found not in compliance were sediment in street or gutters, sediment in drain inlets, concrete washout not maintained and uncovered stockpiles (Table 27).

Overall, the SWPPPs lacked specificity to insure primary sediment control and containment of overland flow.  A majority of the plans left issues of erosion and sediment control up to the contractor.  This deficiency in direction may lead to inappropriate recommendations or lack of proper sediment controls.  Although sediment is a major pollutant from constructions sites, non-visible pollutants (NVP) that are bound to

Table 27. Number of each type of non-compliance found at construction sites.

| Type of Non-Compliance | Number of Each Type of BMP Non-compliance Found at Construction Sites |
| --- | --- |
| Concrete washout not maintained | 5 |
| DI with concrete materials | 1 |
| Entrance/exit not stabilized | 2 |
| Landscaping sediment not contained | 2 |
| Portable toilets on or near storm drain | 2 |
| Sediment in Drain Inlets | 5 |
| Sediment in street or gutters | 8 |
| Uncovered stockpiles | 3 |
| Wattles not maintained | 1 |
| Unprotected Slopes | 2 |

sediment particles become a concern when sediment is discharged off-site.  NVP from construction materials may stay suspended in overland flow and will not be contained even with proper erosion control measures.  These concerns should be addressed in the SWPPP design to significantly reduce the potential discharge of NVPs. The two necessary conditions to reduce NVPs is to reduce exposure of their sources and to reduce transport by overland flow.  We make recommendations in this report in other sections about the need to cover waste building materials and to stop the use of “pig pens” at construction sites.  Adopting these recommendations will greatly reduce the exposure of the source of NVPs to rainfall and overland flow.

Reducing the volume of overland flow is difficult and under the best possible conditions, some overland flow will be generated by normal rainfall.  Maintenance of soil infiltration rate by reducing soil compaction and maintaining surface cover will help to maximize infiltration rate and reduce overland flow volume. Once clay size (<2m) material is entrained, it is difficult and expensive to remove it from overland flow.  The best management practice is to reduce detachment of clay-size material from the soil by maintaining adequate soil cover on erodible areas during the rainy season.  Sedimentation ponds are frequently constructed to assist with removal of clay-size suspended sediment, but they often fail because the detention time is insufficient to allow the clay particles to settle.  Chemical treatment to flocculate the particles is possible, but expensive.

The design of a SWPPP takes experience and a substantial understanding of erosion and sediment control practices.  One reason engineers may have difficulty writing site specific SWPPPs may be due to the lack of routine field experience with erosion control issues.  Engineers mostly work on projects during the initial design phase and may not focus on a site’s current and surrounding conditions during active construction.   In contrast, private consultants that work with various erosion and sediment control issues may be more familiar with the specific needs in a SWPPP document because of their routine field encounters with BMP efficacy.  In addition, consultants generally have more field experience out on sites for which they have written plans.  This field experience enables them to see flaws in their SWPPP designs and enable them to make adjustments in future plans.

Since many of the SWPPPs left erosion and sediment controls up to the contractor, BMP costs play a key role on what BMPs are installed.  It has been found that since developers do not see an immediate return from the initial investment of BMP installation, there is little economic incentive for developers to apply erosion controls.  There have been new fees and educational approaches to improve erosion controls, but changes have been slow (Herzog et al. 2000).

Site visits to the active construction sites showed there is little correlation between what is recommended in the SWPPP to what conditions are found on-site.  A majority of the SWPPPs do not include phasing information.  This lack of phasing changes to BMPs leaves contractors to determine sediment controls throughout construction. Based on field observations, the sites that were in the production phase were found to have the most sediment in storm drains and contaminated runoff in the streets and gutters.  The use of pigpens (uncovered and/or uncontained trash receptacles used on construction sites) were observed having paint residues, concrete bags, silicone caulking, stucco materials and many other wastes generated from construction activities.  Additional research is needed to determine the full range of materials and associated chemicals in off-site discharge.

The most severe problem found on construction sites was the general lack of good housekeeping.  Good housekeeping techniques and procedures are used to control or minimize the potential for pollutant discharge off-site.  Good housekeeping requires sites to be maintained and that workers keep up on inspections and training.  Many sites in this study were found with sediment in the roadways from construction activities.  The lack of drain inlet maintenance and general street sweeping to remove sediment from the roadways and gutters was a major problem in a majority of sites (Table 27). Although many of the inspections were conducted during working hours, some inspections were done before and during rain events and confirmed that responsible personnel on sites were not performing general site inspections and BMP maintenance before storm events.  The use of wattles was common throughout many construction sites, but their continued function is unclear.  Many wattles appeared to be not functioning due to an excessive amount of sediment trapped in them, chronic smashing of wattles from construction vehicles, and removal during landscaping activities.

During the inspections the worst housekeeping was found in areas where construction was almost complete or in locations with little area for storage, such as apartment complexes.

Kaufman (2000) looked at the effectiveness of Michigan’s soil erosion control law and how the law related to slope stabilization, soil stability and water management.  Through his study it was discovered that there is a general lack of integrating “existing technical knowledge of erosion processes and control with policy” (Kaufman 2000).  Of the 30 sites examined in that study, only four performed above the mean of the scoring scale.  The problems found with California’s storm water program are therefore not state specific, but are a nation wide problem as found in Kaufman’s study.

Task 5.  Develop and or propose new alternative strategies to divert flow, reduce or eliminate exposures and for treatment of contaminated storm water prior to release.

Numerous field and laboratory studies have evaluated the efficiency, effectiveness, and performance of erosion and sediment control BMPs. Drawing conclusions from the tests results can be difficult. A review and analysis of these numerous BMP studies concludes that inconsistent study methods and reporting can make wide scale assessments difficult, if not impossible (Strecker, 2000). Furthermore, the author states that different monitoring strategies and data evaluation significantly contribute to the range of BMP effectiveness found among these many studies. As a supplement to these field and laboratory studies, surveys of erosion control professionals and managers can provide a window on the perception of construction site BMP success and performance.

A 2002 survey of 27 Iowa County Engineers asked respondents to list successful and unsuccessful erosion and sediment control measures. The largest number of respondents (44%) selected silt fence as an unsuccessful BMP. At the same time, the largest number of respondents (26%) selected silt fence as a successful BMP. Three BMPs were second among those most frequently selected. Each was listed by 11% of respondents: seeding, rip rap, and matting (Muste, 2002).

Paterson’s 1990 survey of 34 North Carolina Erosion and Sediment Control Administrators found that only 3 out of 11 construction site practices were considered to be good or excellent: sediment basin (94%), sediment trap (73%), and riprap channel (72%). Administrators chose pre-fabricated silt fence, straw bale, and brush barrier as the worst performers (Paterson, 1994).

The 2003 Montana DOT survey of 16 state DOT personnel asked respondents to assess BMP effectiveness. Straw bale was the most often selected ineffective BMP (50%), followed by silt fence (25%), hydroseeding (19%), and silt fence check dams (19%). Blankets and silt fence were the most often selected successful BMPs, listed by 38% of respondents each (MDOT, 2003).

The 1993 survey of 62 state highway erosion control experts by Mitchell asked respondents to rank in order of importance the efficacy of temporary and permanent erosion control measures. The top 3 most effective temporary erosion control methods reported by respondents were hydroseeding with mulching (35%), manual seeding with mulching (21%), and artificial covering (16%). The top 4 most effective permanent erosion control measures were hydroseeding with mulching (27%), manual seeding with mulching (23%), sodding (18%) and riprap (18%) (Mitchell, 1993).

Our findings indicate that before new alternative strategies are created, changes need to be made in how SWPPPs are submitted, approved, and implemented.  It is clear from the results from task 4 that the system for logging SWPPPs does not work well.  We recommend that SWPPPs be submitted electronically and that they proscribe what must be part of the SWPPP before it is approved.  Once approved, additional inspectors are needed to insure that the best management practices are properly implemented and maintained during the course of construction.

We recommend that individuals who implement BMPs be properly trained so that the erosion control materials are installed properly.  Most important is that the erosion control materials be maintained.  Frequently, BMPs failed because the erosion control materials were not maintained or were removed to provide equipment access.

Strategies to Reduce Impact of Construction Site Pollutants on Water Quality

Construction and erosion control materials used on construction sites can release pollutants into storm water. The specific pollutants, modes of release, and strategies to control their release are different for each of these two categories of materials.

The primary characteristic of an effective erosion control material or method is twofold: interception of raindrop energy and slowing of overland flow. Numerous, well researched Best Management Practice guidance manuals provide detailed descriptions, diagrams and instructions on the proper application, installation, location and maintenance of specific and effective materials and methods to control erosion and sediment (see Tables 38 and 39). Many of these manuals are available online and frequently updated so there is no reason to repeat that information here. Alternative strategies, whether a method, material or a policy, are those that are not integrated into commonly used BMP manuals or those that are included in manuals but not used or are overlooked. Our recommended alternative strategies include policy changes, education, refinement of specific methods, and enforcement of non-toxic material use. The best and most appropriate strategies, when properly implemented, installed and maintained, are those described in currently available BMP manuals.

On a larger scale, effective strategies embrace both education and enforcement by combining good construction site housekeeping, proper installation and maintenance of BMPs, enforcement of BMPs, site specific Storm Water Pollution Prevention Plans, use of non-toxic, biodegradable materials and appropriate selection and application of materials to site specific conditions.

Erosion and dust control materials of greatest concern to storm water quality are those materials most commonly used by contractors or used in the greatest quantity, are the most mobile, and are the most harmful to aquatic life. From our contractor surveys, we found wattles (83% of respondents) and blankets (63% or respondents) the most commonly used erosion control materials on construction sites. These products are made with natural materials. With their high C:N ratio, we do not expect release of N into the environment. Both items, when properly installed and maintained, have low water quality impacts. Loose materials, such as liquids, powders and fibers, have a greater potential for degrading water quality. Of the materials in this category, survey respondents used mulch and fibers (56%), dust suppressants (36%), tackifiers (30%), soil drying agents (18%), and soil binders (14%). Many of the liquid and powder products are proprietary mixtures, the ingredients and their concentrations unknown. Most manufacturers do not supply environmental data and very few provide aquatic toxicity LC50 values for their products. Without specific water quality tests that report aquatic toxicity for these brand name products, it is difficult to rank their potential harm to the environment. Recommendations can be made based on laboratory leachate studies and product testing research, although they may be less specific or direct. Total quantities used by survey respondents of these materials are also difficult to rank since amounts used in 2002 were indicated in a variety of units (see Tables 5-12).

Water Quality Issues by Material Type

Mulch & Fibers, Dust Suppressants, Tackifiers & Binders, Green Dye Materials

- Mulch and Fibers:

Water quality concerns for these materials include constituents leached from the mulch or the mulch material itself when removed from a construction site by storm water. When mobilized by storm water, mulch can enter or clog storm drains. Overuse of materials may increase the potential for mobilization. Only one of the 5 brands listed in the survey with an application rate in excess of the manufacturer recommended rate was a mulch product. The other four were tackifiers or binders. Most mulch materials are non-toxic except when ground from treated wood that can leach copper, arsenic, chromium, or pentachlorophenols (see Table 56). Some states, like Pennsylvania, require contractors to use only mulches which have been chemically analyzed and certified (PDOT, 2003). Other materials, both bonded fiber matrix and incorporated wheat straw, can increase TOC and COD in storm water runoff (SDSU, 2000).

Strategies for reducing impact on storm water:

- Avoid overuse of mulch by applying appropriate application rate

- Use blankets on steeper slopes

- Apply mulch, fibers and/or tackifier specific to slope and soil type

- Use organic tackifier in appropriate amounts to immobilize mulch, if necessary, timed to avoid rainfall events

- Use biodegradable mulch with non-toxic dyes

- Require environmental and aquatic toxicity data from manufacturer when using brand name products

- Require certified physical and chemical analyses of all mulch

- Limiting the release of storm water runoff from construction sites with properly installed and maintained BMPs will help prevent TOC and COD increases in storm water runoff due to erosion control material leachates

2)  Dust Suppressants:

The contractor surveys revealed that 36% of respondents (68) used dust suppressants. Of these, 31 indicated composition. Water was the most common dust suppressant (26/31, 84%), followed by magnesium chloride (3/31, 10%), and lignosulfonate (2/31, 6%). The survey showed that few contractors use non-water liquid or powder dust suppressants.

Strategies for reducing impact on storm water:

- Require use of biodegradable, non-toxic dust suppressants

- Require environmental and aquatic toxicity data from manufacturer when using brand name products

- Apply appropriate amounts timed to avoid rainfall events

- Tackifiers and Soil Binders:

In the contractor surveys, six tackifier or soil binder material types were listed by 36 respondents that supplied composition information: plant-based (53%), polymer (36%), petroleum distillate (22%), polyacrylamide (11%), lignosulfonate (3%), and tall oil (3%). Some respondents used more than one type. The top 4 of the 11 brands reported in this category by respondents included Ecology Control M-Binder (15 users), EarthGuard® (8 users), UltraTack™ (4 users), and Soil-Sement® (4 users). Ecology Controls M-Binder, a plant by-product, is made from ground muciloid seed coats. EarthGuard® is a biodegradable copolymer of acrylamide/sodium acrylate with 20.5-22.5% petroleum distillate. UltraTack™, a polymeric anionic polyacrylamide, which has negligible degradation potential and shows limited solubility. Of the 4 top products, only the manufacturer of Soil-Sement®, an acrylic and vinyl acetate copolymer, provided aquatic toxicity data: LC50 (72hr) goldfish 12,500-20,000ppm and LC50 (48hr) Daphnia magna 3,482.8ppm.

For total amount used in 2002 of these products when reported by respondents, see Table 14. Water quality concerns may arise from normal and/or excess application of tackifiers and soil binders. A Caltrans study of seven tackifiers and abinders showed significantly higher measurements for TOC, BOD, Ca and Mg than runoff from bare soil, although Caltrans states that “significance of these va4riations is difficult to ascertain” (Caltrans, 2002). See http://www.dot.ca.gov/hq/env/stormwater/special/newsetup/_pdfs/new_technology/CTSW-RT-02-035.pdf. Significant removal of soil stabilizers and binders from soils by first rainfall events is also a concern (NCSU, 2002; Caltrans 2002). Bare soil plots with or without PAM showed erosion rates 20 times higher after the first seven rain events than those mulched with straw and seeded (NCSU, 2002). Furthermore, slope steepness limits PAM efficacy. Construction site PAM tests with and without mulching on 2:1 slopes failed to show turbidity or erosion reduction (NCSU, 2002). Table 58 contains details from these two studies.

Strategies for reducing impact on storm water:

- Limit PAM used for erosion control to low slopes for short periods

- Select highest quality PAM for site and soil specific conditions

- Apply appropriate amounts (.5 to 1 lb of PAM per 1,000 gallons of water) even though manufacturer recommends 3 to 5 lb of PAM, (California Storm Water BMP Handbook)

- Time application of PAM since efficacy progressively declines with each rainfall event

- Require use of non-toxic, biodegradable tackifiers, soil binders and soil stabilizers

- Require environmental and aquatic toxicity data from manufacturer when using brand name products

Mulch and tackifier may contain green dye for metering when hydroseeding or hydromulching. Toxicities of these dyes (Table 21) are based on the dye alone, not when bound to fiber or particulate materials. Four out of five show LC50 values <1mg/L. Because we found no studies that investigate the environmental fate of these dyes when bound to mulch fibers, we cannot at this time determine their ultimate safety. One mulch dye manufacturer, Amerimulch, explains that the color is designed to last one season. Fading of color over time results from decomposition of the fiber, not from the washing or wearing away of the dye. The manufacturer also points out that some contractors leave colored mulch in large piles before use, which doesn’t allow the mulch dye to dry out. Consequently, driveways are left with stains from the dye. If the dye is resistant to biodegradation, as is C.I. Basic Green 1, what is the ultimate fate of this dye and its effect on the environment? Most manufacturers do not supply information about biodegradation, fate and aquatic toxicity of mulch dyes. Some states require contractors to use only materials with non-toxic green dye. In the Pennsylvania Department of Transportation’s Construction Specifications, wood fiber must be “tinted with nontoxic, green dye and containing an organic tackifier approved for use with wood fibers” (PDOT, 2003). Additionally, recycled cellulose fiber, and cellulose/wood fiber mixtures must also contain nontoxic green dye. On a more positive note, mulch with non-toxic, biodegradable dyes are available to contractors.

Strategies for reducing impact on storm water:

- Use mulch and tackifier with biodegradable, non-toxic green dye

- Require environmental and aquatic toxicity data from manufacturer when using brand name products

Strategies to Reduce The Impact of Construction Materials

on Storm Water

Non-visible pollutants from construction materials are released into storm water when uncovered materials, supplies and waste are exposed to storm water or are released into storm drains during cleaning operations. Preventing contact of these materials with storm water and proper cleaning of equipment decreases the need to sample and analyze storm water for construction material pollutants since the materials are not exposed to storm water or released into storm drains. Stopping pollutant release at their source is the simplest, easiest and cheapest solution for protecting storm water quality.

Strategies for reducing impact on storm water:

- Require covers for all waste receptacles

- Eliminate “pig pens”

- Locate waste receptacles and outhouses away from storm drains

- Require covers for stockpiles

- Install and maintain equipment cleaning areas away from storm drains

- Provide Spanish labels and instructions on all waste receptacles and cleaning areas

- Use green building materials, specifically, those that do not leach harmful constituents

- Provide incentives and education on use of green building materials

When Water Quality is Compromised by Construction Site Pollutants

Strategies for Sampling and Analysis

To fully appreciate the variety of potential leachates from building materials, their waste, and construction materials created from waste, one should examine Table 56. This collection of laboratory and field studies on construction materials lists constituents found in laboratory leachates and storm water runoff. If building materials and/or waste are exposed to storm water, due to poor construction site housekeeping, they can potentially leach pollutants like those in Table 56. In this instance, storm water runoff may require sampling and analysis. When the exposed building material or waste is identifiable or known (paint, solder, lime, soil amendments, etc.), constituents of concern must be selected for testing and analysis. For a list of water quality indicators associated with common non-visible pollutants on construction sites, see Table 3-2 of the Caltrans Construction Site Storm Water Quality Sampling Guidance Manual, http://www.dot.ca.gov/hq/construc/stormwater/SamplingGuidanceManual.pdf.  The manual recommends that the composition of the specific construction material, if known, is the first criterion for selecting which analysis to use. Additionally, pollutants and materials listed in Table 56 can supplement the Caltrans indicator list.

When the exposed building material or waste is not identifiable, as in an uncovered “pig pen” waste receptacle, selection of specific constituents for testing and analysis is difficult or impossible. In this case, all potential non-visible pollutants should be selected for testing, like those listed in Table 31. Although expensive, this is the cost of poor housekeeping. Furthermore, high laboratory test fees may encourage better housekeeping on construction sites. The non-visible pollutants listed in Table 31 originate from the List of Common Potential Non-visible Pollutants at Construction Sites (Table B-1) in the California Storm Water Quality Task Force Construction Storm Water Sampling and Analysis Guidance Document, Appendix C, August 2003, http://www.cabmphandbooks.com/Documents/Construction/Appendix_C.pdf.  Because this list contains common non-visible construction site pollutants, it would be a good place to start in the selection of tests and analyses.

When pollutants in storm water runoff are unknown, sampling and analysis can help establish the source of the pollutant. By examining the water quality indicators and their source materials in the three tables discussed above (CSWQTF, Caltrans and Table 56 of this report), the pollutant source can be narrowed. With this knowledge, contractors can track down the pollutant source and eliminate the problem.

Education and Enforcement

Policy Strategies for Reducing Impact of Construction Materials on

Storm Water

The most effective deterrents to sediment and pollutant release from construction sites combine education and enforcement. An Australian study focusing on the reduction of storm water pollution from construction sites found that building site practices improved significantly in municipalities that implemented an information/education program followed by an enforcement program. As a consequence of this program, the percentage of sites with sediment leaving the site decreased from 71% to 28%. In another finding, the percentage of sites with suitable waste receptacle lids increased from 17% to 41%. The study confirms earlier findings that education alone is ineffective in initiating improvements in construction site practices that reduce sediment and pollutant release (City of Victoria, 2003). For the entire study, see http://www.clearwater.asn.au/resources/371_1.pdf. Similarly, a North Carolina study of 17 construction sites in three counties examined the effectiveness of different environmental policies, regulations and incentives on reducing sediment in nearby streams. The findings suggest that enforcement style and frequency of inspections are significantly more important to stream quality than the stringency of regulations in each of the three counties. Developers prefer a flexible, problem-solving approach with regulators, rather than a rigid, command and control enforcement style. In addition, the study found that fines are ineffective in protecting water quality (Reice, 2000). The authors make the following recommendations:

- Provide sufficient inspectors to visit each construction site at least weekly

- Give inspectors the authority and knowledge to implement innovative solutions to erosion problems on a site-specific basis

- Empower the inspectors to issue severe penalties (stop-work orders) in the case of sedimentation violations

- Raise the maximum level of fines to a meaningful amount

- Educate the development community to the damage that sedimentation does to stream communities

Summary of Alternative Strategies

Materials & Methods, Education, and Policy

Materials Selection:

By initiating mandatory use of non-toxic, environmentally-friendly erosion and dust control materials, the SWRCB can play an important role in the improvement of storm water runoff quality. All categories of materials have biodegradable, non-toxic products on the market. In addition, by holding manufacturers accountable, they will increase their efforts to provide environmental data and environmentally-friendly products to their customers.

Methods for Erosion and Pollution Control:

By initiating mandatory use of closed and covered waste receptacles on construction sites, the SWRCB can play another important role in the improvement of storm water runoff quality. Labels and waste management instructions in Spanish will help laborers comply with rules and best management practices. Other erosion control methods may require fine-tuning. Overuse of materials can also compromise water quality. Contractors should be aware of manufacturer recommended rates, even though they believe that more is better. Lastly, appropriate use of materials, by slope, soil type, and by timing with rainfall will help preserve water quality.

As an alternative strategy to ease the challenges of construction site housekeeping, we recommend that contractors “contract out” their housekeeping duties. We propose a solution that may help the industry reduce NOVs and fines while keeping costs low.  The proposed solution may also go far to reduce toxic chemical release to runoff water from construction sites. The solution is construction site maid service. Contractors with one or more NOVs should be required to hire an independent construction site maintenance service to oversee housekeeping and erosion control BMP upkeep during the rainy season. Duties would include many of the infractions that we observed on our construction site visits such as covering waste and stockpiles, maintaining entrances and exits, managing toilet placement, replacing crushed wattles, street sweeping, storm drain clearing, and concrete washout patrol, etc. By removing worst offenders from their list, inspectors would have fewer sites to manage that were also better maintained. Most important, this would ensure a decrease in storm water runoff and improve runoff quality from the worst sites, without hiring more inspectors. Contractors would then be more “green” and would save the cost of litigation and fines.

Education:

Persistence in the education of contractors and laborers is paramount, both in the proper installation and maintenance of BMPs, in the reasons for erosion and sediment control, and in the selection of environmentally friendly building and erosion control materials.

Policy:

Enforcement is essential, although expensive. Implementation of the discussed strategies above will decrease the work-hours necessary for enforcement and inspection. Other policy strategies that can facilitate oversight, inspection, and accountability on construction sites include electronic submittal of SWPPPs, agency review of all SWPPPs, and centralized collection, database storage, and analysis of storm water runoff test results from construction sites.

Task 6.  Draft cost-effective and fair methodology for storm water sample collection and analysis report

Introduction and general recommendations

Water sampling and monitoring requirements vary for visible and non-visible pollutants in storm water. Waste and stockpiles exposed to storm water can potentially leach a variety of pollutants (see Building Pollutant Table 20). Furthermore, evidence from construction site visits (Task 4) show that the commonly used uncovered “pig pen” waste receptacles contain a range of building material & supply debris. Consequently, whether or not waste and stockpiles on construction sites are covered will affect the selection and number of tests performed on the sample.

Visible Pollutants

Our investigation of active construction sites revealed three main visible storm water pollutants in streets, gutters and drains: sediment, straw mulch debris, and concrete washout water. If sampling and testing of storm water is required, a number of scenarios are possible, some of which include the following:

- If waste and stockpiles are covered, test only for sediment.

- If waste and stockpiles are uncovered, test for sediment and all non-visible pollutants in Laboratory Test Table (Table 31).

- If waste and stockpiles are covered and storm water is gray, test for pH.

- It waste and stockpiles are covered, though concrete washout area is not maintained or doesn’t exist, test for pH.

Non-Visible Pollutants

Non-visible pollutants in construction site runoff can originate from waste piles, building materials and supplies, concrete washout, vehicle maintenance, pesticides, portable toilets, erosion control materials and road building materials (Pollutant Table 20). Our investigation of active construction sites found BMP non-compliance that would result in the release of non-visible pollutants into storm water runoff. As with visible pollutants, if waste and stockpiles are uncovered, test for all non-visible pollutants in Laboratory Test Table, unless a spill of a known material has occurred. For construction sites that are well maintained with all BMPs in compliance, test selection for non-visible pollutants in storm water runoff will require more thought and research. For example, erosion control material or dust suppressant composition and solubility information can be found in our Access database. This data may help narrow laboratory test selection for a particular constituent. If SWPPPs required contractors to list all materials used in erosion and dust control as well as all materials used in construction that were left in uncovered disposal areas, then inspectors would have prior knowledge of what materials to test for.  Without that information, it is impossible to predict what NVPs might be in storm water. When specific building materials are known to contribute to storm water pollution, the Caltrans “Pollutant Testing Guidance Table” can provide information on pollutant indicators, suggested field analyses and laboratory tests for numerous construction site building materials. See

http://www.dot.ca.gov/hq/construc/stormwater/sw_attachments/attachment_s.doc.

Cost Effectiveness

Cost effectiveness of laboratory vs. on-site testing depends upon how often a construction site will need storm water runoff testing, the number of constituents that need testing, the availability of trained construction site personnel for on-site testing, and whether or not sampling and monitoring is outsourced. By utilizing the cost and fee information in the Access Laboratory, Sampling and Equipment tables (Tables 48, 63, and 64), contractors can estimate which method is most cost effective for monitoring storm water runoff at their construction site.

Independently derived pollutant leachate, aquatic toxicity, and environmental data (biodegradation, bioaccumulation, solubility, etc.) from all building materials, dust suppressants and erosion control materials, especially brand name products that are proprietary mixtures are needed to fully design best management practices.

Storm Water Runoff Test Results

If the California Water Resources Control Board were able to receive copies of storm water runoff test results, an enormous amount of data could be accumulated that might help answer questions about which pollutants are found in construction site runoff.

To better understand the costs relating to storm water collection and analysis, we gathered price and product information on water sampling and water monitoring devices. With this information, we examined cost effectiveness by comparing manual (grab) sampling to automatic sampling devices. In the investigation of cost effective storm water monitoring, we collected laboratory fee data for visual and non-visual storm water pollutants and compared the costs of laboratory use with the costs of on-site field monitoring.

Information on types and amounts of construction and erosion control material leachates in storm water runoff are needed to fully design best management practices.

Water Sampling Devices, Monitoring Equipment, & Laboratory Fees

Product and price information for storm water sampling and monitoring equipment were gathered from manufacturer and distributor web sites and by telephone conversations with manufacturers or their distributors. Prices varied among distributors. Laboratory fee data were collected from web sites, by email questionnaire or through telephone conversations with the laboratory.  The tables and fields in the Access database are listed in Table 28.

Table 28. Sampling device, monitoring equipment and laboratory fee data contained in three Access tables.

| Table Name | Fields |
| --- | --- |
| Water Sampling Devices | Product Name, Product Type, Price, Weight, Power Source, Telemetry, www, Notes |
| Water Monitoring Equipment | Product Name, Product Type, Analytes, DO, pH, Conductivity, ORP, Turbidity, Resistivity, Salinity, TDS, Total Dissolved Gas, Depth, Barometric Pressure, GPS, Price, Power Source, Memory, Range, Communication, Unattended Logging, www |
| Laboratory Fees | ID, County, Turnaround, TSS, Setteable Solids, Turbidity, Oil & Grease, pH, Conductivity, TDS, Alkalinity, Residual Chlorine, VOCs, SVOCs, Phenols, MBAS, Phosphates, Phosphorus, Pesticides, Herbicides, Metal (Title 22), Chromium VI, Metals (Individual), NO3, NH3, BOD, COD, TOC, Total Coliform |

# Water Sampling Devices

The Water Sampling Device table (Table 64) provides price and product information on nine power-operated and three mechanically operated portable storm water sampling devices. Both types of samplers allow retrieval of the sample at a later time.

Description and Costs

Mechanical: With no power requirements, passive mechanical devices collect first flush samples or may be adjusted to collect time-weighted composite samples. They can be placed in the ground, situated in a pipe or suspended from a grate. Prices for the three mechanical samplers vary between $355 and $757.

Automatic: Automatic storm water samplers range from the simple to the complex and comprehensive. All require a power source, usually battery, though a few allow solar panel hook-ups.  Storm water samples from these devices may be discrete, composite or a combination of the two. Collection bottles may be single or multiple, usually with a choice of polyethylene or glass. Programming allows for flow-weighted, time-weighted, or water-level triggering of devices by flow meter or rain gauge attachments. Additional features include data logging, refrigeration, telemetry, and multi-parameter sonde attachment. Several samplers provide alerts to email, pagers or cell phones. One device collects samples for VOC testing. Prices for the eight non-VOC samplers range from $895 to $5,900. The VOC storm water sampler costs $7,000. See Table 29 for an example from the Access Water Sampling Devices table.

# Water Monitoring Equipment

## The Water Monitoring Equipment table provides price and product information on 46 portable devices, including both in-situ and handheld equipment, suitable for monitoring visible and non-visible pollutants in storm water runoff (Table 63). All are battery operated. Most require calibration and maintenance. The products are organized into five main types: Single Parameter Handheld (12 items), Multi-Parameter Handheld (14 items), Photoionization Monitors (3 items), Photometers (11 items), and Sondes/Probes (6 items).  See Table 30 for an example from the Access Water Monitoring Equipment table.

Description and Costs

Single Parameter Handheld: Numerous products exist on the market for single-parameter water quality monitoring. Typical parameters available include pH, turbidity, chlorine, dissolved oxygen, oxidation-reduction potential, total dissolved solids, conductivity, or salinity. The 12 items in this category include 6 turbidity meters, 5 pH meters and 1 chlorine meter. Most of the turbidity meters measure 0 to 1,000 NTUs with ± 2-3% accuracy. Other capabilities may include data storage, unattended logging or an RS-232 port for downloading data to a computer. Prices range from $675 to $1,950.  Two types of pH meters are listed in the table: spot-checkers with electrode and meter in one unit and handheld devices with a sensor attached by cable to a meter. Most measure 0.00 to 14.00 pH with ± 0.01 pH accuracy and include temperature.  The two spot-checkers are the most economical at $75 and $275. Those with separate sensor, cable and meter units range from $250 to $525.

Multi-Parameter Handheld: Of the 14 multi-parameter devices listed in the table, 12 are of the sensor-cable-meter style and two are palm-sized with meter and electrodes in one unit. Exchangeable sensors arranged in various configurations allow these devices to simultaneously measure a combination of 4 to 13 of the following parameters: dissolved oxygen, pH, conductivity, ORP, TDS, resistivity, salinity, total dissolved gas, turbidity, temperature, depth, or barometric pressure. Additionally, two can test for specific ions: NO3-, NH4+, Cl-, F-, K+, Ca2+.  Other capabilities may include data storage, remote monitoring, GPS, unattended logging, or an RS-232 port for downloading data to a computer. Prices range from $125 to $7,500; more specifically, 5 products are $125-$1,000, 5 products $1,001-$3,000, and 4 products are $3,001-$7,500.

Photoionization Monitors:  The three handheld devices listed in the table can monitor VOCs in water typically through measurement of the head-space in collected water samples. All have data storage and RS-232 ports. The most sensitive of the three can measure VOC levels of 0.1 to 10,000 ppm and 1 to 999 ppb. Prices range from $2,995 to $3,245.

Photometers:  The table lists 11 portable colorimeters and spectrophotometers that can test for a variety of analytes, three of which can test for more than 90. Those of interest to storm water monitoring include numerous metals, nitrate, ammonia, ammonium, phosphate, organophosphonate, phosphorus, COD, TOC, phenols, surfactant, MBAS, alkalinity, petroleum hydrocarbons, and herbicide. Additionally, several can test for suspended solids, DO, pH, turbidity, conductivity, and salinity. Most include an RS-232 port. Three offer data storage. Prices range from $495 to $1,995 with 8 below $1,000 and 3 above $1,000.

Sondes & Probes:  These in-situ devices collect water quality data, usually for long-term, unattended monitoring. Sensors fit into probes that are then placed in a sonde. These devices can measure up to 17 parameters simultaneously including DO, pH, conductivity, ORP, TDS, resistivity, salinity, total dissolved gas, turbidity, ammonia, ammonium, nitrate, chloride, open channel flow, and temperature. Of the 6 products listed in the table, all have internal data storage, RS-232 and SDI-12 ports. Several offer GPS and remote monitoring. Prices range $2,150 to $7,510.

Laboratory Test Fees

Six State Certified Laboratories with offices in eight counties were selected from the California Department of Health Services web site for pricing information. Table 31 provides a summary of the average price and price range for tests of visible and non-visible pollutants listed in Appendix B of the Construction Storm Water Sampling and Analysis Guidance Document, August 2003.  The specific fees for each of the six laboratories are contained in the Access table called Laboratory Fees and the summary data in Table 31 are contained in the Access table called Laboratory Fee Summary. Turnaround time for test results ranges from 5 to 20 days, the average for all six laboratories is 12 days.

Table 29. Example of Storm Water Sampling Device characteristics.

| Type | Product Name | Price | Weight | Power | Telemetry | www | Notes |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Battery Operated | Global Storm water Sampler SS201 | 995.00 | 22 lbs. | 12 AH gel cell, minimum 4 months | no | http://www.globalw.com/ss101.html | Sample is triggered by rain gauge or raised water level in storm drain. Includes two 4,000ml polyethylene bottles: takes first flush sample in one bottle and a time-weighted composite sample in the second bottle. |
| Battery Operated | Hach Sigma 900 Portable Wastewater Samplers | 2,036.00-2,471.00 | 28 lbs. | 12 VDC or AC adapter, 5 year lithium battery | yes | http://www.americansigma.com/products /dowloads/aws3405.pdf | Program by time or flow. Can collect composite or discrete samples. Polyethylene or glass bottles in a single or multiple bottle (up to 24) configuration. Can store up to five sampling programs and 400 sample collection times/dates. For remote communications and data transfer via wireless cell modem, the Sigma 1000 Wireless Remote Monitor can track significant events in multiple locations. |

Table 30. Example of Water Monitoring Equipment table.

| Type | Name | Price | Power | Memory | Range | Communications | Unattended Logging | www |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Handheld, Multi-Parameter | DKK-TOA WQC-24 Multi-Parameter Water Quality Meter | 3,495.00 | 2 AA batteries or AC adapter (meter); 3 AAA batteries (sensor) | stores 3,360 data sets; logging at 15 minute intervals for 35 days |  | RS-232, remote monitoring | yes | http://www.coleparmer.com/ catalog |
| Handheld, Single-Parameter | LaMotte 2020 Portable Turbidity Meter | 795.00 | 9 V alkaline battery with AC adapter |  | 0 to 1,100 NTU | RS-232 |  | http://www.lamotte.com/ pages/domwat/2020.html |
| Photometer | Hach DR/890 Colorimeter | 929.00 | 4 AA alkaline batteries, six | stores 50 readings |  | RS-232 |  | https://ecommerce.hach.com/stores/ hachpdfs/Literature/L1983.pdf |

Table 30. (continued)

| Type | Name | Test Factors | DO Mg/L | DO %Sat | pH | Conduct-ivity | ORP | TDS | Turbid-ity | Resist-ivity | Salinity | TDG | Baro-metric Pressure | GPS | Depth |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Handheld, Multi-Parameter | DKK-TOA WQC-24 Multi-Parameter Water Quality Meter | NO3-, Cl-, F-, Ca2+, K+, NH4+, chlorophyll | yes | yes | yes | yes | yes | yes | yes | no | yes | no | no | yes | yes |
| Handheld, Single-Parameter | LaMotte 2020 Portable Turbidity Meter |  | no | no | no | no | no | no | yes | no | no | no | no | no | no |
| Photometer | Hach DR/890 Colorimeter | 90+ analytes, including metals, ammonium, chlorine, COD, surfactant, fluoride, hardness, hydrazine, nitrate, nitrite, ammonia, oxygen demand, phosphate, phosphonates, phosphorus, silica, sulfate, sulfide, suspended solids, tannin and lignin, TOC, triazole, volatile acids |  |  |  |  |  |  |  |  |  |  |  |  |  |

Table 31. Average price and price range of laboratory tests for six state certified laboratories.

| Lab Test | Average Price per analysis | Price Range per analysis |
| --- | --- | --- |
|  | $ |
| Alkalinity 310.1 | 18.00 | 10.00-25.00 |
| BOD 405.1 | 46.00 | 25.00-75.00 |
| Chromium VI 7196 | 93.00 | 75.00-110.00 |
| COD 410.1,410.2, or 410.4 | 31.00 | 10.00-50.00 |
| Conductivity 120.1 | 17.00 | 10.00-25.00 |
| Herbicides 8151 | 198.00 | 125.00-275.00 |
| MBAS 425.1 | 48.00 | 25.00-85.00 |
| Metals, Individual ICP | 25.00 | 10.00-50.00 |
| Metals, Title 22 | 232.00 | 200.00-285.00 |
| NH3 350.1,350.2, or 350.3 | 39.00 | 25.00-65.00 |
| NO3 300.0 | 32.00 | 15.00-50.00 |
| Oil & Grease 413.1,413.2 or 1664 | 90.00 | 40.00-150.00 |
| Pesticides 8081A | 155.00 | 120.00-200.00 |
| pH 150.1 | 16.00 | 7.00-25.00 |
| Phenols 420.1 | 78.00 | 33.00-150.00 |
| Phosphates 300.0 | 35.00 | 15.00-50.00 |
| Phosphorus 365.2 | 36.00 | 25.00-30.00 |
| Residual chlorine 330.5 | 28.00 | 15.00-50.00 |
| Setteable Solids 160.5 | 22.00 | 10.00-35.00 |
| SVOCs 8270C | 314.00 | 180.00-450.00 |
| TDS 160.1 | 22.00 | 10.00-30.00 |
| TOC 415.1 | 50.00 | 40.00-75.00 |

Table 31. (continued)

| Lab Test | Average Price per analysis | Price Range per analysis |
| --- | --- | --- |
| Total Coliform SM9221B or SM9221E | 53.00 | 30.00-90.00 |
| TSS 160.2 | 22.00 | 10.00-30.00 |
| Turbidity 180.1 | 19.00 | 10.00-30.00 |
| VOCs 8260 | $179.00 | $100.00-$275.00 |

## Cost Effective Sampling

There are two options for sampling storm water runoff: manual (grab sample) or automatic. Costs for equipment, labor, training and maintenance vary for each method. The quality of the samples may also vary. Although manual sampling has low equipment costs, labor costs are higher than for automatic sampling. With automatic sampling, labor costs are lower yet equipment, training and maintenance are much higher. As an additional advantage, automatic samplers can ensure sample and data collection for all rainfall events, and thereby save on fines when manual samples are missed. One manufacturer’s cost comparison of manual versus automatic storm water sampling finds that automatic samplers pay for themselves by reducing labor costs. In the analysis, a 22-acre site with four sampling stations and eight months of seven rain events required $3,680 (labor) and $610 (equipment) for manual sampling and $940 (labor) and $4,770 (equipment) for automatic sampling. The automatic sampling costs in this study do not include set up, maintenance and training. Though initial equipment costs are much higher for automatic sampling, costs disappear the following year and return only when new equipment is needed.

For more details on this study, see http://www.stormwatersamplers.com/pdf/Manual%20vs%20Automatic%20Sampling.pdf

Mechanical storm water collection devices, like the three listed in the Water Sampling Device table, can provide a simpler and much cheaper alternative ($355 to $757) to automatic sampling for contractors who want to avoid sending out personnel for grab samples unnecessarily. However, sending out personnel during rainfall events, unnecessarily or not, will help contractors keep abreast of construction site runoff.

Manual storm water sampling is the most cost effective method for well-maintained construction sites with little storm water runoff.  As the number of rainfall events that lead to construction site runoff increases, and therefore, the number of samples that need collection, automatic sampling becomes more cost effective. Mechanical devices, if used properly, are the most economical and require little training.

Long term water quality monitoring has shown that frequent samples are required over a long time period to develop a quantitative picture of stream water quality.  Such intensive sample collection is not cost effective for construction sites, especially small sites that are active for a short time.  One possible strategy would be to contract with consulting firms or university researchers to establish monitoring of selected large-scale developments.  The cost could be jointly shared by the SWRCB and the contractor or land owner.  Over time, a well documented history of impacts of construction could be developed and the efficacy of BMPs determined.

## Cost Effective Monitoring

Field monitoring of storm water runoff can offer a contractor timely and useful data. In contrast, test results from a laboratory make take 5 to 20 days. Because many of the portable devices require training and maintenance, some contractors may not have the option of field monitoring and will need to rely on laboratory test results.

Visible pollutants: Visible pollutants, like sediment, alert the contractor to runoff problems right away, which can then be attended to promptly. If the contractor needs this visual observation verified and/or quantified, a variety of field instruments can monitor turbidity and suspended solids. Six portable turbidity meters and two photometers for suspended solids measurement are listed in the Access Water Monitoring Equipment table. One of the photometers can measure both items. Comparing average laboratory test costs for TSS and turbidity, the photometer that measures both suspended solids and turbidity would pay for itself after 23 uses. The cheapest turbidity meter would pay for itself after 36 uses. Because the photometer can be used for numerous other tests, it could potentially pay for itself after many fewer uses.

Non-visible pollutants: Non-visible pollutants in storm water runoff are more varied (see Table 31), more difficult to pinpoint and require more expensive testing than visible pollutants. The non-visible pollutants listed in Table 31 originate from the List of Common Potential Non-visible Pollutants at Construction Sites (Table B-1) in the California Storm Water Quality Task Force Construction Storm Water Sampling and Analysis Guidance Document, Appendix C, August 2003, http://www.cabmphandbooks.com/Documents/Construction/Appendix_C.pdf.  Since this list contains common non-visible construction site pollutants, it would be a good place to start in the selection of tests and analyses. The appropriate tests depend entirely on what materials are used in construction and what materials are exposed to rainfall. Few, if any of these tests is related to a single pollutant and hence knowledge of the materials used on the site is critical to making appropriate analytical choices.

Most NVPs result from poor construction site housekeeping, such as improper waste storage and management, equipment/vehicle maintenance and washing, fueling, spill management, materials handling and storage, stockpile management, sanitary/septic waste management, and herbicide/pesticide management.

Erosion control materials themselves may also be a source of non-visible pollutants.

Blankets & Mulch: Elevated TOC and COD were measured in runoff from wood fiber blanket, straw-coconut blanket, straw blanket, bonded-fiber matrix, and incorporated wheat straw (see Access Product Testing Sources, SDSU report, Table 58).  Analytical tests (Table 31) for total organic carbon, chemical or biochemical oxygen demand or specific carbon compounds would be appropriate in cases where blankets and mulches have been used for erosion control.

Polyacrylamides: According to the California Stormwater BMP Handbook, polyacrylamides, when improperly used or over-used, may be considered a non-visible pollutant. The handbook recommends that polyacrylamides designated for erosion and sediment control be water soluble and pass through a sediment control BMP before discharging to surface water. In addition, the Handbook suggests application rates of no more than .5 to 1 lb. of polyacrylamide per 1,000 gallons of water per acre even though manufacturers may recommend 3 to 5 lbs. The one survey respondent that supplied application rate information for a polyacrylamide product used 5 lbs./acre and also commented that more works better. Timing of polyacrylamide application is also of concern since efficacy progressively declines with each rainfall event. The NCSU study (see the Access Product Testing Sources, Table 58) recommends limiting use to low slopes for short periods. Ultimately, contractors should use only the highest quality polyacrylamides that are site and soil specific.

In locations where polyacrylamides or other chemical tackifiers are used, it is appropriate to test storm water for either the original material or decomposition products of the materials (Table 31).

Survey Materials: For chemical/composition information on brand name products listed in the surveys, we created two tables condensing information from our Access tables on these materials. Table 32 organizes composition/chemical information gleaned from manufacturer’s product information and Table 33 supplements that table with chemical/solubility/aquatic toxicity data on the chemicals listed as major constituents in the MSDS sheets of these products. Many manufacturers do not list chemical ingredients on MSDS sheets. Survey brands soluble in water include Dustac® 100, Dust-Off®, and Terra-Lock™ 50.

Table 32. Product information from manufacturer.

| Product | General Composition | Ecological Information | pH | Water Solubility |
| --- | --- | --- | --- | --- |
| Dustac® 100 | calcium lignosulfonate | biodegradable | 4-5 | soluble |
| Dust-Off® | magnesium chloride, magnesium sulfate | unknown | 6.5 | complete |
| EarthGuard® | copolymer of acrylamide/sodium acrylate; petroleum distillate (20.5-22.5%), sodium metabisulfite (0.6-0.8%) | biodegradable | unknown | dilutable |
| Ecology Controls M-Binder | ground muciloid seed coat | unknown | unknown | negligible |

Table 32. (continued)

| Product | General Composition | Ecological Information | pH | Water Solubility |
| --- | --- | --- | --- | --- |
| Envirotac II® Soil Stabilizer | acrylic co-polymer (39-43%), residual monomers (<0.1%), ammonia (<1.0%) | unknown | 5.0 to 9.5 | dilutable |
| PolyPavement™ | vinyl acrylic copolymer (96+%) emulsifier (1+%), surfactant (1+%) | emulsifier and surfactant are biodegradable; CA Dept. of Fish & Game Test#LN-93-48-1: LC50@7,450ppm | unknown | insoluble/dilutable |
| Soil Master WR | polyvinyl acetate | unknown | unknown | unknown |
| Soil-Sement® | acrylic and vinyl acetate polymer(5-50% by wt) | LC50(72hr) goldfish 12,500-20,000ppm; LC50(48hr) Daphnia magna 3,482.8ppm | 4.0-9.5 | dilutable |
| Terra-Lock™ 50 | sodium acrylate/acrylamide copolymer(50%) dispersed in mineral oil, petroleum distillates (35% by wt), surfactant, impurities include acrylic acid (<0.5% by wt) and acrylamide(<0.10% by wt) | biodegradable | 7.5 (1% solution) | soluble |
| TOPEIN™S | tall oil by product (42-48% by wt), nonylphenol polyethylene glycol ether as surfactant, hydrochloric acid | LC50(96hr) fish 400mg/L, EC50(72hr) fresh water algae 1000mg/L, EC50(48hr) Daphnia magna 2000mg/L; biodegradable | 6-8 | insoluble |
| UltraTack™ | anionic polyacrylamide, | degradation potential is limited | unknown | limited |

When non-visible pollutants in storm water runoff require identification, it would be helpful to determine their source, and thereby narrow the number and specificity of tests.  It is possible for a number of these tests to be done on-site. By looking at a worst-case scenario, the cost effectiveness of field monitoring can be evaluated. If the construction site is a housekeeping disaster and storm water runoff requires monitoring, testing for a full range of pollutants will be necessary. Photometers can test for a number of the pollutants listed in Table 31.  For example, if the Hach DR/2400, the most expensive photometer ($1,995), is used to measure all the items in Table 24, excluding BOD, pesticides, turbidity, settelable solids, alkalinity, TDS, SVOCs, and coliform, the device would pay for itself by two uses. Test results may be stored and downloaded to a computer for record keeping. On a smaller scale, if a contractor finds that a recent application of magnesium chloride dust suppressant coincides with a rainfall event, monitoring runoff with the Hanna 98129 Combo conductivity/pH meter ($125) would pay for itself after seven uses, not including any pH measurements.

If high laboratory test fees encourage good housekeeping, then contractors should use a laboratory when testing for non-visible pollutants in storm water runoff, though laboratory tests may be less useful for the contractor since they are not timely. On the other hand, if poor housekeeping is readily apparent and the contractor promptly improves the situation, then timeliness may not be important.

Laboratory testing is the most cost effective method for monitoring storm water runoff on well-maintained sites with little runoff. In contrast, construction sites with the most runoff producing rainfall events, the worst housekeeping, and the poorest management of erosion control materials will require the most storm water monitoring. Field monitoring with portable devices is the most cost effective method for these high maintenance sites and provides contractors with timely information that may help manage construction sites and minimize runoff problems.

Table 33. Product chemical, solubility and toxicity information.

| Product Name | Major MSDS Chemical | Water Solubility | Aquatic Toxicity |
| --- | --- | --- | --- |
| Dustac® 100 | calcium lignosulfonate | soluble in water | LC50/96hr/Oncorynchus mykiss (rainbow trout)/5,200ppm. (British Columbia Ministry of Environment) |
| Dust-Off® | magnesium chloride | 543g/L@20C | Aquatic toxicity: LC50/48hr/Leuciscus idus melanotus (fresh water fish)/7700mg/L; LC50/48hr/Gambusia affinis (fresh water fish)/17750mg/L; EC50/24hr/Daphnia magna/3190mg/L; LC50/25hr/Daphnia magna/3391mg/L; EC50/72hr/Scendesmus subspicata (algae)/2200mg/L. (ECB) |
|  | magnesium chloride hexahydrate | 1670g/L@25C | unknown |

Table 33. (continued)

| Product Name | Major Chemical | Water Solubility | Aquatic Toxicity |
| --- | --- | --- | --- |
| EarthGuard® | distillates (petroleum), hydrotreated light | 15mg/L@20C | Biodegradation: 4-12% after 28 days. Aquatic toxicity: LC50/96hr/Pimpephales promelas (fresh water fish)/45mg/L; LC50/96hr/Lepomis macrochirus (fresh water fish)/1740mg/L; LC50/48hr/Salmo sp./1.60mg/L; LC50/96hr/Diatomus forbesi (invertebrate)/140mg/L; EC50/15day/Anabaena doliolum (algae)/5.97mg/L. (ECB) |
| Terra-Lock™ 50 | sorbitan oleate | <10g/L@20C | Biodegradable |
|  | acrylamide/sodium acrylate polymer | highly soluble in water | unknown |
|  | distillates (petroleum), hydrotreated light naphthenic | very low | Biodegradation: 6% after 28 days. Inherently biodegradable in water, but not readily so. In water, the substance is likely to be adsorbed onto particulate matter, and will ultimately be biodegraded by micro-organisms. Aquatic toxicity: LC50/96hr/Oncorhynchus mykiss (fresh water fish)/>5000mg/L; LC50/96hr/Salmo gairdneri/>1000mg/L; EC50/96hr/Daphnia magna/>1000mg/L; EC50/96hr/Scenedesmus subspicatus (algae)/>1000mg/L. (ECB) |

Maid Service: Construction Site Housekeeping Alternative

Our investigation of BMPs revealed extensive poor housekeeping on construction sites, a task difficult for some contractors even after several Notice of Violations (NOV) or large fines. Furthermore, some contractors would rather pay large fines than stop construction site work. With the current system, the question remains; to what degree do NOVs and fines stop BMP non-compliance and repeat offenders?

We propose a solution that may help the industry reduce NOVs and fines while keeping costs low.  The proposed solution may also go far to reduce toxic chemical release to runoff water from construction sites. The solution is construction site maid service. Contractors with one or more NOVs should be required to hire an independent construction site maintenance service to oversee housekeeping and erosion control BMP upkeep during the rainy season. Duties would include many of the infractions that we observed on our construction site visits such as covering waste and stockpiles, maintaining entrances and exits, managing toilet placement, replacing crushed wattles, street sweeping, storm drain clearing, and concrete washout patrol, etc. By removing worst offenders from their list, inspectors would have fewer sites to manage that were also better maintained. Most important, this would ensure a decrease in storm water runoff and improve runoff quality from the worst sites, without hiring more inspectors. Contractors would then be more “green” and would save the cost of litigation and fines.

Task 7.  Final version of the cost-effective and fair methodology for sample collection and analysis report.

This report serves as the final version.

Final Summary

To investigate the types and amounts of materials used for erosion and dust control on California construction sites, we examined product data, surveyed contractors and manufacturers, reviewed SWPPPs and inspected construction sites. A literature search of building material impacts on storm water quality provides additional information on potential non-visible pollutants. These data, along with BMP non-compliance findings on construction sites, help clarify water sampling cost-effectiveness and issues.

## Erosion and Dust Control Materials on Construction Sites

Our assemblage of erosion and dust control product information for blankets, mulches, liquids and powders, demonstrates the multitude and variety of materials available to contractors and erosion control professionals. Because liquid and powder products have the highest potential for degrading water leaving a construction site, most of the composition, solubility and toxicity data pertain to these materials.  Because most liquids and powders are mixtures, the ingredients and percent composition often remain proprietary secrets. In addition, the availability of information on environmental attributes, decomposition and fate of these mixtures is also lacking. Only 22% of manufacturers supply environmental information on product sheets, MSDS or websites.

The four largest categories of liquid or powder products on the market include plant & animal based materials (52 items), vinyl acetate or acrylic copolymers (35 items), polyacrylamides (32 items),  and petroleum products (21 items). Results from the manufacturer survey show that all of these categories are sold in California. Many are soluble in water, including polyacrylamides, petroleum products, polyvinyl acetate polymers, lignin polymers, salt solutions, wetting agents, enzyme products, and most plant and animal based products.  Occasionally manufacturers provide aquatic toxicity information (LC50) for their products: petroleum products (28-510 mg/L), polyacrylamides (15-1,000 mg/L), polyvinyl acetate materials (100-3,482 mg/L), vinyl acrylic copolymer (7,450 mg/L), and a wetting agent (>1,000 mg/L). In the contractor survey, the 11 brand name products named by respondents belong to the following categories: vinyl acrylic copolymers (4 users), plant based products (3 users), petroleum products (2 users), and polyacrylamides (2 users). Most liquids and powders are applied as tackifiers, soil binders or soil drying agents and are used by 55% of survey respondents. Of the contractors using dust suppressants (36%), 38% of these respondents use water. Other liquid and powder materials listed in the survey include lime (10% of respondents) and fly ash (2% of respondents). In addition to type of material usage, the survey also indicates that some contractors apply more than the manufacturer recommended rate for tackifiers and binders. Our inspections of active construction sites found that 25% of contractors used tackifiers.

As with liquids and powders, contractors can also choose from a variety of mulches and fibers (64 items). Most are composed of wood fibers though other constituents may include polyester or polypropylene fibers, newsprint, recycled wood, recycled paper, cotton fiber, corn fiber, straw, shredded tires, wetting agents, tackifier, petroleum distillates and green dye. In our survey, 56% of respondents use an assortment of mulches made from wood fiber, wood chips, polyester fiber, straw, paper, sawdust, stable waste, recycled green waste and yard waste. Some of the wood fiber and straw mulch users add tackifier. As with tackifiers, some contractors apply more than the manufacturer recommended rate. Non-brand application rates for mulch range from 0.75 to 2 tons per acre. On active construction sites, 19% applied straw mulch and 13% used hydroseeding.

Blanket, mat, netting, and geotexile products (102 items) are numerous and varied. Materials may include straw, coir fiber, wood fiber, corn fiber, jute, aspen, recycled plastic, rayon, polyolefin, polyester, nylon, polypropylene, and wire. In our survey, 63% of respondents use blankets, mats or netting. Of those reporting specific materials, the four largest types listed include straw blankets (14 users), jute netting (13 users), straw with coconut fiber blankets (11 users), and coconut fiber blankets (10 users). On active construction sites, 25% of contractors used blankets or geotextiles.

Wattles, the most widely used product, are manufactured in a variety of widths and lengths, usually from straw or coir fiber, encased in coir or poly netting (11 items). One product is made from aspen excelsior. In our survey, 83% of respondents use wattles. Of those reporting a specific type, 85% are made from straw. On active construction sites, 69% of contractors used wattles.

With an availability of numerous tackifiers, binders and dust suppressants, contractors can choose materials with low solubility and low concentrations of harmful constituents that will biodegrade and not bioaccumulate.

## Building Materials on Construction Sites

Building materials and their waste, as revealed by the literature, can add to urban storm water pollutant loads. By substituting environmentally friendly building materials for those known to leach harmful constituents, contractors can play an important long-term role in improving storm water runoff quality. Furthermore, by covering waste and stockpiles, contractors prevent known leachates from entering storm water. The continual accumulation of information on all construction site materials, including data on constituents, solubility, toxicity, bioaccumulation and biodegradation, will help regulators keep abreast of non-visible storm water runoff quality from construction sites.

## Best Management Practices on Construction Sites and SWPPPs

Our examination of 32 Storm Water Pollution Prevention Plans and 16 active construction sites in three California counties added to our investigation of good housekeeping best management practices currently used on construction sites.

The seven most frequently found BMPs on the 16 construction sites include the following: gravel bags (12 sites), wattles, (11 sites), silt sacs (5 sites), blankets (4 sites), concrete washout (4 sites), tackifier (4 sites), and straw mulch (3 sites). In the SWPPPs, the seven most frequently drawn or indicated BMPs include the following: wattles (21 plans), silt fence (15 plans), entrance/exit stabilization (12 plans), straw mulch (8 plans), gravel bags (8 plans), tackifier (8 plans), and staging area (8 plans).

For installation guidance, contractors may consult a plethora of BMP manuals published by city and county agencies or independent consultants. We examined 13 manuals from 11 states to investigate BMP priorities outside of California. Over 165 methods and materials are identified. Seven BMPs are described in at least 12 manuals: blankets, check dams, construction entrances, slope drains, inlet protection, mulching, and silt fences.

## BMP Non-Compliance on Construction Sites

In addition to BMP selection and use, the construction site visits also revealed types and quantities of BMPs not in compliance. Overall, more than half of sites (69%) showed BMP non-compliance. We observed ten BMP types not in compliance: the top four included sediment in street or gutter (50%), concrete washout not maintained (31%), sediment in drain inlet (31%), and uncovered stockpiles (19%).

## SWPPP Issues

Our review of 32 SWPPPs revealed a number of problems with the SWPPP process, database, and quality of the documents.

Of the 75 “active” construction sites selected from the California State Water Quality Control Board web site SWPPP database, 10 (13%) were no longer active or had wrong addresses. Furthermore, a straight-forward “request for SWPPP” letter to property owners sent by Region 5 RWQCB retrieved only 50% of the remaining 65.

The 32 SWPPPs received showed a range in quality, primarily in depth, detail and site specificity. All were graded 1 to 5 (poor to excellent): poor (9%), below average (38%), average (28%), good (6%), and excellent (19%). Almost 50% were below average or poor in quality. The process for creating submitting, reviewing and approving SWPPPs should be improved.  We recommend that SWPPPs be submitted electronically and that the contents be proscribed so that they are site specific.  Once submitted and approved, inspections should be made to insure that the recommended BMPs are properly implemented and maintained.

Strategies to Reduce Impacts from Erosion Control Materials & Construction Materials on Storm Water

Erosion and dust control materials of greatest concern to storm water quality are those materials most commonly used by contractors or used in the greatest quantity, are the most mobile, and are the most harmful to aquatic life. From our contractor surveys, we found wattles (83% of respondents) and blankets (63% or respondents) the most commonly used erosion control materials on construction sites. These products are made with natural materials. With their high C:N ration, we do not expect release of N into the environment. Both items, when properly installed and maintained, have low water quality impacts. Loose materials, such as liquids, powders and fibers, have a greater potential for degrading water quality. Of the materials in this category, survey respondents used mulch and fibers (56%), dust suppressants (36%), tackifiers (30%), soil drying agents (18%), and soil binders (14%). Many of the liquid and powder products are proprietary mixtures, the ingredients and their concentrations unknown. Most manufacturers do not supply environmental data and very few provide aquatic toxicity LC50 values for their products. Without specific water quality tests that report aquatic toxicity for these brand name products, it is difficult to rank their harm to the environment. Recommendations can be made based on laboratory leachate studies and product testing research, although they may be less specific or direct. Total quantities used by survey respondents of these materials are also difficult to rank since amounts used in 2002 were indicated in a variety of units (see Tables 5-12).

The following are recommendations for limiting the pollution originating from materials used on construction sites.

Mulch and Fibers:

- Avoid overuse of mulch by applying appropriate application rate

- Use blankets on steeper slopes

- Apply mulch, fibers and/or tackifier specific to slope and soil type

- Use organic tackifier in appropriate amounts to immobilize mulch, if necessary, timed to avoid rainfall events

- Use biodegradable mulch with non-toxic dyes

- Require environmental and aquatic toxicity data from manufacturer when using brand name products

- Require certified physical and chemical analyses of all mulch

- Limiting the release of storm water runoff from construction sites with properly installed and maintained BMPs will help prevent TOC and COD increases in storm water runoff due to erosion control material leachates

Dust Suppressants:

- Require use of biodegradable, non-toxic dust suppressants

- Require environmental and aquatic toxicity data from manufacturer when using brand name products

- Apply appropriate amounts timed to avoid rainfall events

Tackifiers and Soil Binders:

- Limit PAM used for erosion control to low slopes for short periods

- Select highest quality PAM for site and soil specific conditions

- Apply appropriate amounts (.5 to 1 lb of PAM per 1,000 gallons of water) even though manufacturer recommends 3 to 5 lb of PAM

- Time application of PAM since efficacy progressively declines with each rainfall event

- Require use of non-toxic, biodegradable tackifiers, soil binders and soil stabilizers

- Require environmental and aquatic toxicity data from manufacturer when using brand name products

Materials with Green Dye:

- Use mulch and tackifier with biodegradable, non-toxic green dye

- Require environmental and aquatic toxicity data from manufacturer when using brand name products

Other Education and Enforcement Strategies:

- Require covers for all waste receptacles

- Eliminate “pig pens”

- Locate waste receptacles and outhouses away from storm drains

- Require covers for stockpiles

- Install and maintain equipment cleaning areas away from storm drains

- Provide Spanish labels and instructions on all waste receptacles and cleaning areas

- Use green building materials, specifically, those that do not leach harmful constituents

- Provide incentives and education on use of green building materials

- Provide sufficient inspectors to visit each construction site at least weekly

- Give inspectors the authority and knowledge to implement innovative solutions to erosion problems on a site-specific basis

- Empower the inspectors to issue severe penalties (stop-work orders) in the case of sedimentation violations

- Raise the maximum level of fines to a meaningful amount

- Educate the development community to the damage that sedimentation does to stream communities

References

Azizian, M.F., P.O. Nelson, P. Thayumanavan, and K.J. Williamson. 2003. Environmental Impact of Highway Construction and Repair Materials on Surface and Ground Waters: Case Study: Crumb Rubber Asphalt Concrete. Waste Management, 23:719-728.

Bae, B., J.H. Jeong, and S.J. Lee. 2002. The Quantification and Characterization of Endocrine Disruptor Bisphenol-A Leaching From Epoxy Resin. Water Science and Technology 46 (11):381-387.

Birst, S., and J. Hough. 1999. Chemical Additive Usage on Unpaved Roads in the Mountain Plains States. Upper Great Plains Transportation Institute Publication No. 130.

Boller, M. 1997. Tracking Heavy Metals Reveals Sustainability Deficits of Urban Drainage Systems. Water Science & Technology 35(9):77-87.

Boller, M.A., and M. Steiner. 2002. Diffuse Emission and Control of Copper in Urban Surface    Runoff. Water Science and Technology 46(6-7):173-181.

Boyer, B.W. 1994. Alkaline Leachate and Calcareous Tufa Originating from Slag in a Highway Embankment Near Baltimore, Maryland. Transportation Research Record 1434:3-7.

Bucheli, T.D., S.R. Muller, A. Voegelin, and R.P Schwarzenbach. 1998. Bituminous Roof Sealing Membranes as Major Sources of Herbicide (R,S,)-Mecoprop in Roof Runoff Waters. Environmental Science & Technology 32(22):3465-3471.

Caltrans 2002. Caltrans Hydraulic Application Study. State of California Department of Transportation. Sacramento, CA.

Caltrans 2003. Construction Site Storm Water Quality Sampling Guidance Manual. State of California Department of Transportation. Sacramento, CA. Available at http://www.ca.gov/hq/construc/stormwater/SamplingGuidanceManual.pdf

Carr, R.L., L.L. Ho, and J.E. Chambers. 1997. Selective Toxicity of Chlorpyrifos to Several Species of Fish During an Environmental Exposure: Biochemical Mechanisms. Environmental Toxicology and Chemistry 16(11):2369-2374.

Cherry, D.S., J.H. Van Hassel, P.H. Ribbe, and J. Cairns, Jr. 1987. Factors Influencing Acute Toxicity of Coal Ash to Rainbow Trout (Salmo gairdneri) and Bluegill Sunfish (Lepomis macrochirus). Water Resources Bulletin 23(2):293-306.

Chugh, Y.P.,	 B.C. Paul, V.K. Puri and J. Mukherjee. 1994. Evaluation of the Mixtures of AFBC Fly Ash and Coarse Coal Refuse as a Construction Material For Embankments. Conference Proceedings: Management of High Sulfur Coal Combustion Residues: Issues and Practices, April 5-7, 1994, Springfield, IL.

City of Victoria 2003. Regulating Building-Site Practices to Reduce Stormwater Pollution. Victoria, Australia. Available at http://www.clearwater.asn.au/resources/371_1.pdf

Corish, K.A. 1995. Clearing and Grading Strategies for Urban Watersheds. Metropolitan Washington Council of Governments. Washington, D.C. 54pp.

Daniel, T.C.,	 P.E. Mc Guire, D. Stoffel, and B. Miller. 1979. Sediment and Nutrient Yield From Residential Construction Sites. Journal of Environmental Quality 8(3):304-308.

Davis, A.P., M. Shokouhian, and S. Ni. 2001. Loading Estimates of Lead, Copper, Cadmium, and Zinc in Urban Runoff From Specific Sources. Chemosphere 44:997-1009.

Demond, A.H.	1985. Leaching of Tetrachloroethylene from Vinyl-Lined Pipe. Journal of Environmental Engineering, Vol. 111(1):1-9.

Deutsch, Y., and Y. Nathan. 2001.Time-Related Changes in Coal Ash in Two Embankments and a Roadbase. International Ash Utilization Symposium, October 22-24, 2001, Lexington, KY.

Donohue, I., E. Verheyen, and K. Irvine. 2003. In Situ Experiments On the Effects of Increased Sediment Loads on Littoral Rocky Shore Communities in Lake Tanganyida, East Africa. Freshwater Biology  48(9):1603-1616.

Duble, R.L., J.C. Thomas, and K.W. Brown. 1978. Arsenic Pollution From Underdrainage and Runoff from Golf Greens. Journal of Agronomy 70(1):71-74.

Eldin, N.N. 2002. Road Construction: Materials and Methods. Journal of Environmental Engineering 128(5):423-430.

Erosion and Sediment Control Field Manual. 2002. California Regional Water Quality Control Board San Francisco Bay Region. Oakland, CA. 148pp.

Ferreira, C., A. Ribeiro, and L. Ottosen. 2003. Possible Applications For Municipal Solid Waste Fly Ash. Journal of Hazardous Materials  B96:201-216.

Fisher, T.S., D.G. Hayward, R.D Stephens, and M.K. Stenstrom. 1999. Dioxins and Furans Urban Runoff. Journal of Environmental Engineering 125(2): 185-191.

Forster, J. 1996. Patterns of Roof Runoff Contamination and Their Potential Implications on Practice and Regulation of Treatment and Local Infiltration. Water Science & Technology 33(6):39-48.

Forster, J. 1999. Variability of Roof Runoff Quality. Water Science & Technology 39(5):137-144.

Forsyth, D.S., and B. Jay. 1997. Organotin Leachates in Drinking Water from Chlorinated Poly(vinyl chloride) (CPVC) Pipe. Applied Organometallic Chemistry 11(7):551-558.

Garcez, I., M.E. Tittlebaum, and J.M. Momtgomery. 1987. Leachability of Lignite Fly Ash Enhanced Road Base. Journal of Environmental Science and Health Part A 22(7):607-625.

Garrick, N.W.,	 and K. Chan. 1993. Evaluation of Domestic Incinerator Ash for Use As Aggregate in Asphalt Concrete. Transportation Research Record 1418:30-34.

General Permit. National Pollutant Discharge Elimination System General Permit for Storm Water Discharges Associated With Construction Activity. California State Water Resources Control Board Water Quality Order 99-08-DWQ. Available at http://swrcb.ca.gov/stormwtr/docs/finalconstpermit120602.pdf.

Goh, A.T.C.,	 and J. Tay. 1993. Municipal Solid-Waste Incinerator Fly Ash For Geotechnical Applications. Journal of Geotechnical Engineering 119(5):811-825.

Good, J.C. 1993. Roof Runoff as a Diffuse Source of Metals and Aquatic Toxicity in Storm Water. Water Science & Technology 28(3-5):317-321.

Gromaire, M.C., G. Chebbo, and A. Constant. 2001. Impact of Zinc Roofing On Urban Runoff Pollutant Loads: The Case of Paris. NOVATECH International Conference on Innovative Technologies in Urban Drainage, June 25-27, 2001, Lyon-Villeurbanne, France.

Grossman, R.F., and G.R. Mitchener. 1996. Migration of Metal-Containing Additives From Vinyl to the Soil. Regulatory Issues in the Plastics Industry: Health, Safety and the Environment Technical Papers, Regional Technical Conference - Society of Plastics Engineers,1996, Brookfield, CT.

Harbor, J.M.,	 J. Snyder, and J. Storer. 1995. Reducing Nonpoint Source Pollution from Construction Sites Using Rapid Seeding and Mulching. Physical Geography 16:371-388.

Heebink, L.V.,	 and D.J. Hassett. 2001. Coal Fly Ash Trace Element Mobility in Soil Stabilization. 2001 International Ash Utilization Symposium, October 22-24, 2001, Lexington, KY.

Herzog, M., H. Harbor, K. McClintock, J. Law, and K. Bennett. 2000. Are Green Lots Worth More Than Brown Lots? An Economic Incentive for Erosion Control on Residential Developments. Journal of Soil and Water Conservation 55(1):43-50.

Hingston, J.A., C.D. Collins, R.J. Murphy, and J.N. Lester. 2001. Leaching of Chromated Copper Arsenate Wood Preservatives: A Review. Environmental Pollution 111:53-66.

Izquierdo, M.,	 E. Vazquez, X. Queol, M. Barra, A. Lopez, and F. Plana. 2001. Use of Bottom Ash from Municipal Solid Waste Incineration as a Road Material. International Ash Utilization Symposium, October 22-24, 2001,  Lexington, KY.

Kalyoncu, R.S. 2002. Coal Combustion Products - Production and Uses. Proceedings of Coal Combustion By-Products and Western Coal Mines: A Technical Interactive Forum. U.S. Department of Interior, April 16-18, 2002, Golden, CO.

Kaneko, H. 1996. Evaluation of Municipal Waste Incinerator Fly Ash Toxicity and the Role of Cadmium by Two Aquatic Toxicity Tests. Waste Management 16(5/5):555-559.

Karlen, C., I.O. Wallinder, D. Heijerick, C. Leygraf, and C.R. Janssen. 2001. Runoff Rates and Ecotoxicity of Zinc Induced by Atmospheric Corrosion. The Science of the Total Environment 277:169-180.

Kaufman, M.M. 2000. Erosion Control at Construction Sites: The Science-Policy Gap. Environmental Management. 26(1):89-97.

Kim, A.G. 2002a. CCB Leaching Summary: Survey of Methods and Results. Proceedings of Coal Combustion By-Products and Western Coal Mines: A Technical Interactive Forum. U.S. Department of Interior, April 16-18, 2002, Golden, CO.

Kim, A.G. 2002b. Physical and Chemical Characteristics of CCB. Proceedings of Coal Combustion By-Products and Western Coal Mines: A Technical Interactive Forum. U.S. Department of Interior, April 16-18, 2002, Golden, CO.

Krenitsky, E.C., M.J. Carroll, R.L. Hill, and J.M. Krouse. 1998. Crop Science 38:1042-1046.

Kszos, L.A., G.W Morris, and B.K. Konetsky. 2004. Source of Toxicity in Storm Water: Zinc From Commonly Used Paint. Environmental Toxicology and Chemistry 23(1):12-16.

Lahl, U. 1992. Recycling of Waste Foundry Sands. The Science of the Total Environment 114:185-193.

Lalor, M., and S.E. Clark. 2003. Watershed Protection Through Building Material Substitution and Controlled Use. Auburn University Environmental Institute. U.S. Geological Survey Water Resources Grant Proposal ID: 2002AL1B. Available at http://water.usgs.gov/wrri/02grants/prog-compl-reports/2002AL1B.pdf.

Lind, B.B., A.M. Fallman, and L.B. Larsson. 2002. Environmental Impact of Ferrochrome Slag in Road Construction. Waste Management 21:255-264.

Lopes, T.J., J.D Fallon, D.W. Rutherford, and M.H. Hiatt. 2000. Volatile Organic Compounds in Storm Water From a Parking Lot. Journal of Environmental Engineering 126(12):1137-1143.

MDEP, Maine Department of Environmental Protection. 2004. Erosion & Sedimentation Control Law: A Report to the 121st Maine Legislature. Available at http://www.maine.gov/dep/blwq/report/04escreport.pdf.

MDOT, Montana Department of Transportation. 2003. Erosion and Sediment Control Best Management Practices: Organizational Structure Survey. Helena, MT. Available at

http://www.mdt.state.mt.us/research/docs/research_proj/erosion/org_survey.pdf.

Milanova, E.,	 S. Wood, and B.B. Sithole. 1997. Toxicity of Newsprint Dyes to Rainbow Trout and Activated Sludge. Tappi Journal 80(5):113-118.

Mitchell, G. 1993. Assessment of Erosion/Sediment Control in Highway Construction Project. Final Report to Ohio Department of Transportation. Columbus, OH. 206pp.

Moo-Young, H., K. Sellasie, D. Zeroka, and G. Sabnis. 2003. Physical and Chemical Properties of Recycled Tire Shreds for Use in Construction. Journal of Environmental Engineering 129(10):921-929.

Mroueh, U., P. Eskola, and J. Laine-Ylijoki. 2001. Life-Cycle Impacts of the Use of Industrial By-Products in Road and Earth Construction. Waste Management 21:271-277.

Mumley, T. 2000. Construction Site Planning and Management Tools for Water Quality Protection. National Conference on Tools for Urban Water Resource Management and Protection Proceedings, February 7-10, 2000, Chicago, IL.

Murarka, I.P.	2002. Environmental Performance of CCPs. Proceedings of Coal Combustion By-Products and Western Coal Mines: A Technical Interactive Forum. U.S. Department of Interior, April 16-18, 2002, Golden, CO.

Muschack, W.	1990. Pollution of Street Run-Off by Traffic and Local Conditions. The Science of the Total Environment 93:419-431.

Muste, M. 2002. Erosion Control for Highway Applications, Phase I: Review and Synthesis of Literature. Iowa Department of Transportation Final Report TR-464. Ames, IA. 76pp. Available at http://www.dot.state.ia.us/materials/research/reports/reports_pdf/hr_and_tr/reports/tr464.pdf.

National Cooperative Highway Research Program (NCHRP). 2000. Environmental Impact of Construction and Repair Materials on Surface and Ground Waters. NCHRP Report 443. National Academy Press. Washington, D.C.

Natusch, D.F.S. 1978. Characterization of Fly Ash from Coal Combustion. Workshop Proceedings on Primary Sulfate Emissions from Combustion Sources. US EPA 600/9-78-020b, 2:149-163.

NCDLR, North Carolina Division of Land Resources. 1998. Inspections. Sediments: Newsletter of the N.C. Sedimentation Control Commission 5(2). Available at http://www.dlr.enr.state.nc.us/vol5no2sed2.html.

Neufeld, R.D.,	and S. Wallach. 1984. Chemical and Toxicity Analysis of Leachates From Coal Conversion Solid Wastes. Journal of the Water Pollution Control Federation 56(3):266-273.

Ohno, T. 1990. Levels of Total Cyanide and NaCl in Surface Waters Adjacent to Road Salt Storage Facilities. Environmental Pollution ENPOEK 67(2):123-132.Paterson, R.G.	1994. Construction Practices: The Good, the Bad, and the Ugly. Watershed Protection Techniques 1(3):95-99.

PDOT 2003. Construction Specifications. Publication 408/2003, Section 805. Commonwealth of Pennsylvania Department of Transportation.

Peyton, R.L., S.H. Anderson, and C.J. Gantzer. 1995. Termiticide Leachate From Building Foundation Drains. Journal of Irrigation and Drainage Engineering 121(5):322-326.

Pitt, R. 2000. Sources of Storm water Pollutants, Including Pollutant Buildup and Washoff. Pp. 3-1 to 3-81. In The Source Loading and Management Model: A Water Quality Management Planning Model for Urban Storm water Runoff. University of Alabama at Birmingham.

Polkowska, Z., Gorecki, T., Namiesnik, J. 2002. Quality of Roof Runoff Waters From a Rural Region (Gdansk, Poland). Chemosphere 49:1275-1283.

Proctor, D.M.,	 E.C. Shay, K.A. Fehling, and B.L. Finley. 2002. Assessment of Human Health and Ecological Risks Posed by the Use of Steel-Industry Slags in the Environment. Human and Ecological Risk Assessment 8(4):681-711.

Quek, U., and J. Forster. 1993. Trace Metals in Roof Runoff. Water, Air, and Soil Pollution 68:373-389.

Reice, S.R., and J. Carmin. 2000. Construction Site Planning and Management Tools for       Water Quality Protection. National Conference on Tools for Urban Water Resource Management and Protection Proceedings, February 7-10, 2000, Chicago, IL.

Ronchak, A. 1990. Waste Tires in Sub-Grade Road Beds: A Report on the Environmental Study of the Use of Shredded Waste Tires for Roadway Sub-Grade Support. Minnesota Pollution Control Agency. St. Paul, MN.

Rosenberry, P.A. Bukavackas, D.C. Buso, G.E. Likens, A.M. Shapiro, and T.C. Winter. 1999. Movement of Road Salt to a Small New Hampshire Lake. Water Air and Soil Pollution 109(1-4):179-206.

Roy, W.R., R.A. Griffin, D.R. Dickerson, and  R.M. Schuller. 1984. Illinois Basin (USA) Coal Fly Ashes: 1. Chemical Characterization and Solubility. Environmental Science Technology 18(10):734-739.

Ruckstuhl, S., M.J.F. Suter, H.E. Kohler, and W. Giger. 2002.  Leaching and Primary Biodegradation of Sulfonated Naphthalenes and Their Formaldehyde Condensates from Concrete Superplasticizers in Groundwater Affected by Tunnel Construction. Environmental Science & Technology 36(15):3284-3289.

Ruiz, M.C., A. Andres, and A. Irabien. 2000. Environmental Characteristics of Ferrous Foundry Wastes. Environmental Technology 21(8):891-899.

Sadecki, R.W., G.P. Busacker, K.L. Moxness, K.C. Faruq, and L.G. Allen. 1996. An Investigation of Water Quality in Runoff From Stockpiles of Salvaged Concrete and Bituminous Paving. Minnesota Dept. of Transportation Report Number MN/PR-96/31. Oakdale, MN.

Sadiki, A., D.T. Williams, R. Carrier, and B. Thomas. 1996. Pilot Study on the Contamination of Drinking Water by Organotin Compounds From PVC Materials. Chemosphere 32(12):2389-2398.

Sadiq, M., T.H. Zaidi, H. Al Muhana, and A.A. Mian. 1997. Effect of Distribution Network Pipe Material on Drinking Water Quality. Journal of Environmental Science and Health A32(2):445-454.

Sadler, R., C. Delamont, P. White, and D. Connell. 1999. Contamination in Soil As a Result of Leaching From Asphalt. Toxicological and Environmental Chemistry 68(1):71-81.

Schreurs J.P.G.M., H.A. van der Sloot, and Ch. Hendricks. 2002. Verification of Laboratory - Field Leaching Behavior of Coal Fly Ash and MSWI Bottom Ash As a Road Base Material. Waste Management 20:193-201.

SCVAS, Santa Clara Valley Audubon Society. 2002. Storm water and Sediment: An Evaluation of San Jose's Construction-site Monitoring and Enforcement Program. Available at http://www.scvas.org/stmwtrnsedbody.pdf.

Show, K., J. Tay, and A.T.C. Goh. 2003. Reuse of Incinerator Fly Ash in Soft Soil Stabilization. Journal of Materials in Civil Engineering 15(4):335-343.

Smith, E.B., and L.K. Swanger. 2000. Toxicity and Worldwide Environmental Regulation of Lead-Free Solder. Transactions of the Institute of Metal Finishing 78(2):18-21.

Solo-Gabriele H., M. Kormienko, and K. Gary. 2000. Alternative Chemicals and Improved Disposal-End Management Practices for CCA-Treated Wood. Florida Center For Solid and Hazardous Waste Management Report#00-08. Gainesville, FL.

Sorme, L., and R. Lagerkvist. 2002. Sources of Heavy Metals in Urban Wastewater in Stockholm. The Science of the Total Environment 298(1-3):131-145.

Sosebee, J.B., P.C. Geiszler, D.L. Winegardner, and C.R. Fisher. 1982. Contamination of Groundwater Samples with Poly(Vinyl Chloride) Adhesives and Poly(Vinyl Chloride) Primer From Monitor Wells. Hazardous and Industrial Solid Waste Testing: Second Symposium, January 28-29, 1982, Lake Buena Vista, FL.

Steffes, R. 1999. Laboratory Study of the Leachate From Crushed Portland Cement Concrete Base Material. Iowa Department of Transportation Report # MLR-96-4. Ames, IA.

Stern, M.S. and  D.H. Stern. 1980. Effects of Fly Ash Heavy Metals on 'Daphnia magna.' Missouri University, Kansas City, MO. National Technological Information Service, PB81-198327.

Strecker, E.,	M.M. Quigley, and B.R. Urbonas. 2000. Determining Urban Storm water BMP Effectiveness. National Conference on Tools for Urban Water Resource Management and Protection Proceedings, February 7-10, 2000, Chicago, IL.

Suloway, J. J.,	T.N. Skelly, W.R. Roy, D.R. Dickerson, R.M. Schuller, and R.A. Griffin. 1983. Chemical and Toxicological Properties of Coal Fly Ash. In: Energy and Environmental Stress in Aquatic Systems. Environmental Geology Notes 105:1-70.

Symonds.1999. Construction and Demolition Waste Management Practices and Their Economic Impacts. Report to DGXI, European Commission. Symonds Group Ltd. Available at

http://europa.eu.int/comm/environment/waste/studies/cdw/c&dw_chapter1-6.pdf.

Taylor, A. 2002. City-wide or Regional Erosion and Sediment Control Programs - What Works. Cooperative Research Centre for Catchment Hydrology. Available at

http://www.ecorecycle.vic.gov.au/asset/2/upload/Andre_Taylor_ESC.doc

Taylor, B.R.,	 J.S. Goudey, and N.B. Carmichael. 1996. Toxicity of Aspen Wood Leachate to Aquatic Life: Laboratory Studies. Environmental Toxicology and Chemistry 15(2):150-159.

Taylor, J.L.,	and P.A. Cooper. 2003. Leaching of CCA from Lumber Exposed to Natural Rain Above-Ground. Forest Products Journal 53(9):81-86.

Townsend, T.G. 2000. Continued Research into the Characteristics of Leachate from Construction and Demolition Waste Landfills. Florida Center For Solid and Hazardous Waste Management Report #00-04. Gainesville, FL.

Townsend T.G., H. Solo-Gabriel, T. Tolaymat, and K. Stook. 2003. Impact of Chromated Copper Arsenate (CCA) in Wood Mulch. The Science of the Total Environment 309(1-3):173-185.

Townsend T.G., Y. Jang, and L.G. Thurn. 1999. Simulation of Construction and Demolition Waste Leachate. Journal of Environmental Engineering 125(11):1071-1081.

van der Sloot H.A. 1991. Systematic Leaching Behaviour of Trace Elements From Construction Materials and Waste Materials. Environmental Implications of Construction with Waste Materials, November 10-14, 1991, Maastricht, The Netherlands.

van der Sloot, H.A. 2000. Comparison of the Characteristic Leaching Behavior of Cements Using Standard (EN 196-1) Cement Mortar and an Assessment of Their Long-Term Environmental Behavior in Construction Products During Service Life and Recycling. Cement and Concrete Research 30:1079-1096.

van der Sloot, H.A., D. Hoede, D.J.F. Cresswell, and J.R. Barton. 2001. Leaching Behavior of Synthetic Aggregates. Waste Management 21:221-228.

van Houdt, J.J.,E.J. Wolf, and R.F. Duzijn. 1991. Composition and Leaching Characteristics of Road Construction Materials. Environmental Implications of Construction with Waste Materials, November 10-14, 1991, Maastricht, The Netherlands.

Vandecasteele, C., K. Van den Broeck, T. Van Gerven, V. Dutre, P. Seuntjens, P. Berghmans, C. Cornelis, and J. Nouwen. 2002. Characterization and Treatment of Roads Covered With Zinc Ashes, Muffle Furnace Fragments and Lead Slags From Former Non-Ferrous Metal Industries in Belgium. Waste Management & Research 20:365-372.

Weber, W.J.,	Y. Jang, T.G. Townsend, and S. Laux. 2002. Leachate From Land Disposed Residential Construction Waste. Journal of Environmental Engineering 128(3):237-245.

Wolman, M.G., and A.P. Schick. 1967. Effects of Construction on Fluvial Sediment, Urban and Suburban Areas of Maryland. Water Resources Research 3:451-464.

Appendices

Appendix 1.	Erosion Control Professional Survey

Appendix 2.	SWPPP Draft Inspection Report

Appendix 3.	Letter requesting SWPPP from contractors

Appendix 4.	Tables from the Access data base

APPENDIX 1 Erosion Control Professional Survey

Date:____________

Company Name:__________________________________________________________

Name of individual completing this survey:____________________________________

Please provide contact information (address, phone, email):________________________

Please check off those products you have used in 2002.

| Material Category | Yes | No |
| --- | --- | --- |
| Tackifiers |  |  |
| Soil binders including fly ash |  |  |
| Soil drying products such as lime |  |  |
| Mulch (including BFM) |  |  |
| Blankets ( mesh, netting, mats, etc.) |  |  |
| Wattles, rolls or logs |  |  |
| Dust suppressant |  |  |

If you did not check off yes on any of these products, you need not continue with this survey.  Please return the survey to us in the self-addressed stamped envelope or FAX it to 530-752-1552.  Thank you for your help.

For each of the material categories you have checked, please list the name of the product, the amount of each product used in 2002 and where in the state the product was used. If you need more room, please use the back of this page.

| Product Name/ Brand Name | Approximation of Amount Used | Application Rate | Location of Use (County/City) | Product Efficacy Comments |
| --- | --- | --- | --- | --- |

May we call you if we need more information?  If so, please give us a contact number.

Thank you.

APPENDIX 2 SWPPP draft inspection report

SWPPP Written By: Consultant, Engineer, self

Site ID #________________

DRAFT

Inspection Record

Scheduling

SWPPP	Start Date______________	End Date__________________ ECM Installed____________ Grading Dates _________

Inspection

Work progressing in accordance with project schedule? YES/NO

Earthwork completed during dry months YES/NO

1-4 mo.	4-6mo.		6-8mo.		8-10mo.	10-12mo.

6-10		4-6		0-4		4-6		6-10

Underground work completed during dry months?  YES/NO

1-4 mo.	4-6mo.		6-8mo.		8-10mo.	10-12mo.

6-10		4-6		0-4		4-6		6-10

If time change have been made is there an amended schedule and changes to BMPs made?  YES/NO

Products added_______________________________________________

Comments

Preservation of Existing Vegetation

SWPPP	Are there planned areas of existing vegetation? YES/NO

Is existing vegetation planned for use as a BMP? YES/NO

Inspection

Is existing vegetation marked off with construction fencing?  YES/NO

Did the site preserve the areas as planned? YES/NO

Comments

Slope Grading

SWPPP	Are there slopes on site?  YES/NO

What is the range of slope ratio? _____________

Is there planned slope protection? YES/NO

What BMP is planned for slope protection? ___________________

Is trackwalking recommended? YES/NO

Inspection

Is planned slope protection in place? YES/NO

Was planned BMP implemented? YES/NO

Has the site been trackwalked? YES/NO

Is trackwalking against contour? YES/NO

Scale: Up-Down 10

Sideways 0

Is the slope terraced?  YES/NO

Length _____________  Depth ________________

Comments

Temporary Seeding & Mulching

SWPPP

Are there proposed areas that will be disturbed & unvegetated during the rainy season? YES/NO

Recommended erosion control for exposed soil areas.___________________________

Inspection

Has temporary seeding or mulching been used? YES/NO

What type_____________________________

Scale: % Cover_________________________

What form of erosion protection is used? __________________________

Comments

Permanent Seeding & Mulching

SWPPP

Are there planned areas for permanent vegetation?

Inspection

Has permanent seeding or mulching been installed? YES/NO

What type_____________________________

Scale: % Cover_________________________

What form of erosion control has been used? ____________________________

Condition: Is it Sluffing off, Sticking

Comments

Hydroseeding/ Hydromulching

SWPPP

Recommended areas for hydroseeding/mulching? YES/NO

Inspection

Vegetable fibers (straw/hay) Hay or straw applied at a rate of 4,500 kg/ha, anchored in with tackifier, netting or crimping.

Wood chips evenly distributed depth of 50mm-75mm

Hydraulic Mulches Recycled paper or wood fiber

Hydraulic Matrices Bonded Fiber Matrix 3,000-4,000 lbs/acre

Was this BMP used?

Does the BMP appear to be working?

% Cover______

Comments

Dust Control

SWPPP

Recommended rate_____________

Recommended method: Water, CaCl2, MgCl2, NaCl, silicates, surfactants, copolymers, petroleum products, Lignin sulfonate, Vegetable oils, spray-on adhesives.

Inspection

What method is being used for dust suppression?

Comments

Erosion Control Blankets

SWPPP	Are there recommendations for ECB? YES/NO

Is it planned for slope/ channel/ outfall

Is a specific product recommended? YES/NO

What product_________________________

Inspection

Slope Ratio: __________

If a channel: Is the channel engineered as directed on site plans?

If a slope: Was the blanket installed from top of slope to toe of slope?

Was the ECB trenched in 6 in. deep and 6 in. wide? YES/NO

Scale_________________________________________

Is there direct contact with the soil? YES/NO

Scale_________________________________________

Comments

Straw Wattles

SWPPP

Are there recommendations for straw wattles?

Inspection

Is there intimate contact with soil? YES/NO

Scale_____________________________

Are the wattles trenched in? YES/NO

What depth?_______________________

Is the extra soil placed on the uphill/ flow side? YES/NO

Are the wattles staked in every 3-5 feet with 1-2” stakes?

Scale____________________________

Do the wattle ends have good contact with each other? YES/NO

Are the wattles maintained well, Condition flat, full of sediment, ineffective, good condition

Comments

Stabilized Construction Entrance

SWPPP

Are the locations of entrances listed on the SWPPP map? YES/NO

Are installation instructions given? YES/NO

Inspection

Entrance elevation lower than street elevation? YES/NO

Angular rock used YES/NO

Is 8” thick course aggregate used? YES/NO

Is there tracking? YES/NO

Is it maintained? YES/NO

Is it working? YES NO

Scale____________________________________________________

Is geotextile used? YES/NO

Is the entrance length a minimum of 50’,

Scale 0-10	10-20		20-30		30-40		40-50+

0-2	2-4		4-6		6-8		8-10

Width (10-15’)

Depth (6-12”)

Comments

Tire Wash

SWPPP

Is a tire wash recommended? YES/NO

Inspection

Is there a tire wash on-site? YES/NO

Comments

Outlet Protection- Energy Dissipation

SWPPP

What type is recommended? ________________________________________

Inspection

Is the pipe unprotected or is there an energy dissipater? YES/NO

What type of energy dissipation is used?________________________________

Comments

Check Dams

SWPPP

Are check dams recommended in the SWPPP? YES/NO

What materials are recommended? ___________________________________

Inspection

Were check dams installed according to recommendations? YES/NO

Scale_______________________________________________

Are the check dams maintained?

What materials are used?

Comments

Silt Fencing

SWPPP

Is silt fencing recommended in the SWPPP? YES/NO

If it is planned in the SWPPP, is it combined with erosion control? YES/NO

Inspection

Constructed along a level contour? YES /NO

Scale_______________________________

Length of slope draining to fence 30m or less? YES/NO

Scale _________________________________________________

Length of single run of fence up to 150m? YES/NO

Scale _________________________________________________

Last 6 ft of fence in J or L shape? YES/NO

Scale _________________________________________________

Fence segments not connected? YES/NO

Scale _________________________________________________

Installation: 2’-5’ from the toe of slope

6”-8” deep YES/NO

trench 4”-6” wide YES/NO

aligned with contours YES/NO

Scale _________________________________________________

Comments

Storm Drain Inlet Protection

SWPPP

Is Inlet protection recommended?

What type of protection is planned for use?

What products are recommended?

Inspection

Is storm DI protection found on every DI? YES/NO

Scale _________________________________________________

Is there a silt sac or equivalent? YES/NO

Scale _________________________________________________

Does the silt sac fit? Scale _________________________________________________

Is silt sac maintained? Scale _________________________________________________

Are they adequate? Scale _________________________________________________

Are there sand/gravel bags/ straw wattle?

Comments

Sediment Basins

SWPPP

Are there sediment basins planned for the project? YES/NO

Have the sediment basins been designed by an engineer? YES/NO

Are there plans on how the site is going to dewater? YES/NO  Type Discharge/ Riser Pipe/evaporation

Inspection

Is there a sediment basin on-site? YES/NO

Does it measure out o what was designed?

What was the plan scale?

Was the plan scale met?

How is the Sediment Basin being dewatered? Discharge/ Riser Pipe/evaporation

Are there secondary BMPs straw/tack or hydroseeding?

% coverage of secondary BMP_________________

Comments

Secondary Filtration

SWPPP

Is secondary filtration recommended? YES/NO

Inspection

Is secondary filtration used on-site? YES/NO

What are the NTUs found in the effluent?___________Inffluent?____________

Comments

Stockpiles

SWPPP

Does the SWPPP discuss stockpile winterization? YES/NO

Inspection

Are stockpiles covered? YES/NO  Type: Plastic/ Hydroseed

Scale _________________________________________________

Are stockpiles surrounded with SW? YES/NO

Scale _________________________________________________

Comments

Concrete Washout

SWPPP

Are recommendations for washout construction included in the SWPPP? YES/NO

Inspection

Does the concrete washout have appropriate signage? YES/NO

Scale _________________________________________________

Is the washout lined? YES/NO

Scale _________________________________________________

Is the washout bermed? YES/NO

Scale_________________________________________________

Located away from storm drain YES/NO

Maintained YES/NO

Is there spillage YES/NO

Comments

Post Construction BMPs

Are there plans for post construction BMPs? YES/NO

APPENDIX 3 Letter requesting SWPPP from contractors

APPENDIX 4 Access tables

Table Number and Title								Page

Table 34 Application Rate		96

Table 35 Ash Aquatic Toxicity		105

Table 36 Bibliography	106

Table 37 Blankets Product Data	113

Table 38 BMP Manuals	116

Table 39 BMP Table	118

Table 40 Brand Name Usage	124

Table 41 Chemical List	1127

Table 42 Contractor Survey General Category Use	125

Table 43 Element Aquatic Toxicity	129

Table 44 Erosion Control Specialist General Category Use	131

Table 45 Green Dye Toxicology	132

Table 46 IECA General Category Use	133

Table 47A Laboratory Fees Part 1	134

Table 47B Laboratory Fees Part 2	135

Table 47C Laboratory Fees Part 3	136

Table 47D Laboratory Fees Part 4	137

Table 47E Laboratory Fees Part 5	138

Table 47F Laboratory Fees Part 6	139

Table 47G Laboratory Fees Part 7	140

Table 48 Laboratory Fee Summary	141

Table 49 Liquids & Powders Chemical Data	142

Table 50 Liquids & Powders Product Data	149

Table 51 Manufacturer Survey General Data	164

Table 52A Manufacturers Part 1	165

Table 52B Manufacturers Part 2	170

Table 53 Manufacturers Survey Products Sold	180

Table 54 Mulch Chemical Data	182

Table 55 Mulch Product Data	184

Table 56 Pollutants (Building Materials)	186

Table 57 Product List	191

Table 58 Product Testing Sources	209

Table 59 Respondent Use By Region	215

Table 60A Survey Data Part 1	216

Table 60B Survey Data Part 2	234

Table 61 SWPPP and Construction Site BMPs	257

Table 62A SWPPP and Construction Site Data Part 1	258

Table 62B SWPPP and Construction Site Data Part 2	263

Table 63A Water Monitoring Equipment Part 1	267

Table 63B Water Monitoring Equipment Part 2	271

Table 63C Water Monitoring Equipment Part 3	273

Table 63D Water Monitoring Equipment Part 4	278

Table 64A Water Sampling Devices	280

Table 64B Water Sampling Devices	281